## Slide 1: Detention Routing

## Slide 2: Objectives
Determine an outflow hydrograph (peak control detention-see map on right) given:
  Inflow Hydrograph (post development)
  Storage and Outflow versus WSE (based on detention basin design)
  Note: Peak control detention must be equal to or less than the pre-development peak

## Slide 3: Detention Basin Components
Inflow (ditch or pipe)
Storage
Outflow (orifice or weir or combination)
Berm
Emergency spillway

## Slide 4: Routing
Method used to model the outflow hydrograph
Is based on the continuity equation (hydraulics)
  Water in varies
  Water out varies
  Storage versus elevation varies

## Slide 5: Information Needed to Route
Inflow hydrograph
Relation of storage volume to water level elevation in the proposed detention basin
Relation of outflow to water level elevation (discharge rating)

## Slide 6: Set up table with small time steps
Water in – Water Out = Difference in Storage
(water in is changing w/ time)
(water out is a function of basin WSE)
(basin WSE is a function of basin geometry)
WSE-water surface elevation

## Slide 7: Reservoir Routing
Over that time step:
Avg Inflow (I) – Avg Outflow (O) = Change in storage per some increment of time
  If I=O there is no change in water elevation
  If I>O then water surface rises
  If I<O then water surface decreases

## Slide 8: Reservoir Routing Over some time increment (1 to 2)
I1 and I2 are inflows at beginning (1) and end (2) of time increment (the entire inflow hydrograph is known)
O1 and O2 are outflows
S1 and S2 are actual storage volumes
Delta t is the time from 1 to 2
Note-variables in red are initially known
We need to solve for O2 and S2

## Slide 9: Equation (1/2)
(I1+I2)/2 – (O1+O2)/2 = (S2-S1)/t
Rearrange to:
(I1+I2) + [(2*S1/t)-O1]=2*S2/t + O2
Left hand side – knowns
Right-hand side - unknowns

## Slide 10: Equation (2/2)
O2 and S2 ; both are unknown; need 2 equations (but we have only one)
However:
We do have a relationship between outflow and storage volume since we determined outflow versus water elevation and the storage elevation versus the water elevation.

## Slide 11: Example Inflow Hydrograph

## Slide 12: Example Storage Vol & Discharge vs WSE
(I1+I2) + [(2*S1/t)-O1]=2*S2/t + O2
Cell G9=(2*7500/1440)-2.5=7.9 cfs
Cell H9=(2*7500/1440)+2.5=12.9 cfs
Note: 1440 is delta t from previous slide; 0.4 hours =1440 seconds

## Slide 13: Volume vs Water Surface Elev.

## Slide 14: Outlet Discharge vs Elevation

## Slide 15: Determining Outflow

## Slide 16: Routing Table
(I1+I2) + [(2*S1/t)-O1]=2*S2/t + O2

## Slide 17: Inflow and Outflow Hydrograph