## Slide 1: CTC 260 Hydrology Introduction

## Slide 2: Objectives
Class Requirements
Drainage Design Overview
Review of Significant Figures
Review of Accuracy and Precision

## Slide 3: Class Requirements
On-Web: http://people.sunypoly.edu/~barans/
Schedule
Lectures
Grades
Brightspace:
Syllabus
Assignments/Dropoffs

## Slide 4: Handouts-Also Online
Hydro-35
TR-55

## Slide 5: Two Parts to Drainage Design
Hydrology – Determine water quantity
Hydraulics – Size structure to handle water

## Slide 6: Drainage Design Steps
Delineate Watershed
Collect Watershed Data
Determine Design Storm
Determine Excess Precipitation (runoff)
Determine Peak Flow
Size Structure

## Slide 7: End of Intro

## Slide 8: Review-Drainage Design Steps
Delineate Watershed
Collect Watershed Data
Determine Design Storm
Determine Excess Precipitation (runoff)
Determine Peak Flow
Size Structure

## Slide 10: Watershed Data
Land Use
Soil Types
Overland flow Length
Length of Channel
Slope
Vegetative Cover
Roughness Coefficient
Existing Storage
Channel Shape
Existing Drainage Structures

## Slide 11: Delineate Watershed
Identify points of interest
  Existing/Proposed Culvert Locations
  Changes in Land Use
  Major Stream Branching
Define Watershed Boundary
Delineate Subcatchment Areas
Determine Drainage Areas

## Slide 12: What is a Watershed
https://www.youtube.com/watch?v=uaZPO7dgEnk

## Slide 13: Design Storm
Return period (frequency)
Precipitation data (quantity/time)
IDF
  Rainfall Intensity
  Storm Duration
  Storm Frequency

## Slide 14: Runoff
Part of design storm will become runoff and part will be retained by watershed (abstraction)
Dependent on:
  Soil type
  Cover type/land Treatment
  Land Use
  Antecedent runoff condition
  Impervious/pervious relationship

## Slide 15: Hydrograph
Graph of time vs direct runoff at one particular location (point of interest)
  Rising limb
  Crest
  Falling (Recessional) Limb

## Slide 16: Hyetograph; Resulting Hydrograph

## Slide 17: Unit Hydrograph
Hydrograph representing 1” of excess precipitation occurring uniformly over the watershed for a specified storm duration

## Slide 18: Ungaged Watershed
If watershed is ungaged, then a synthetic unit hydrograph is developed from empirical equations
Rational Method
TR-55
others

## Slide 19: Peak flow or Hydrograph
Peak flow
Entire hydrograph

## Slide 20: Sizing Drainage Structures
Inlets
Ditches
Culverts
Storm drainage system
Outflow structures
Detention Basin
Open channel flow
Energy/Hydraulic Grade Lines
Friction
Pressure
Head Loss

## Slide 21: Documenting Work
Narrative on what was done and why
Map of watershed delineations
Tables summarizing info
Nomographs/equations used
References

## Slide 22: Significant Figures
Number of digits used to form a quantity
132, 4.01, and 0.00425 all have 3 significant figures
350, 2500, 92,000 all have 2 significant figures
350., 2500., 92,000. have 3, 4, and 5 significant figures, respectively

## Slide 23: Numbers not subject to significant digits
pi
Formulas (2*pi*r)---2 is exact

## Slide 24: Measured numbers-significant digits
229 feet – assumed measured to the nearest foot (could be 228.5 to 229.4); has 3 significant figures
229.5 feet – assumed to be measured to the nearest 0.1 foot (could be 229.45 to 229.54); has 4 significant figures
230 feet
  (2 significant figures; measured to nearest 10 feet)
230. feet
  (3 significant figures; measured to nearest 1 foot)

## Slide 25: Significant Digits-Computation Rules
Multiplication and Division
  Answer should have no more significant figures than the least number of significant figures in any quantity in the computation
Example:
  230.0 x 20. = 460 (2 significant figures; not 460. which would imply 3 significant figures)

## Slide 26: Significant Digits-Computation Rules2
Addition and Subtraction
  Answer should have no more digits to the right of the decimal point than the least number of digits to the right of the decimal point in any quantity in the
Example:
  230.1 + 20. = 250.
  (3 significant figures; not 2; not 4)

## Slide 27: Significant Digits – Computation in Series
Series
  If the answer to one computation is used in another computation, then the final answer is rounded to the quantity with the lowest number of significant digits

## Slide 28: Accuracy and Precision
Accuracy-how close a value is to the actual value
Precision-how many significant digits are displayed
  Avoid displaying lots of numbers because your calculator displays lots of numbers (answer looks precise but is not necessarily accurate)

## Slide 29: Next Lecture
Watersheds
  What are they?
  Why are they important?
  How do you delineate them?
  How do you measure their areas?