## Slide 1: Stormwater Pollution Prevention Plans

## Slide 2: Objectives
Know the brief legislative background of stormwater discharges
Know what a SWPPP is and what is included in a SWPPP

## Slide 3: Definitions
SWPPP-Stormwater Pollution Prevention Plan
NPDES-National Pollutant Discharge Elimination System
SPDES-State Pollutant Discharge Elimination System
MS4-Municipal Separate Storm Sewer System
NOI-Notice of Intent
Blue Book-”New York Standards and Specification for Erosion and Sediment Control”

## Slide 4: Sign for SPEDES Permit

## Slide 5: History
Water Quality Act-1987
  First regulations dealing with discharge of stormwater
Phase I Stormwater Regulations-1990
  NYSDEC is local permitting authority
  NYSDEC issued 2 general permits-1993
    Industrial Site Runoff
    Construction Projects > 5 acres (Phase I)
Phase II Stormwater Regulations-1999
  Apply to Construction Projects > 1 acre

## Slide 6: On-Line References
New York State Stormwater Management Design Manual (Draft 22)
NY Standards and Specifications for Erosion and Sediment Control (Blue Book)

## Slide 7: General Permit
Operator must submit NOI
Operator must prepare SWPPP (water quality and quantity control)
Operator is responsible for implementing all measures outlined in the SWPPP
  Inspections every 7 days and after a storm event of 0.5 inches or more
  Inspection summaries prepared by a “qualified professional” must be posted for view by the public.
  NYSDEC can fine up to $25,000 per day of violation

## Slide 8: Maintaining Water Quality
No increase in turbidity that will cause a substantial visible contrast to natural conditions
No increase in suspended, colloidal and settleable solids that will cause deposition or impair the waters for their best usages
No residue from oils and floating substances, nor visible oil film, nor globules of grease

## Slide 9: Erosion Factors
Soil Type
  Higher potential – silt and fine sand
  Lower potential –clays and organics
Vegetative Cover
Topography
Climate
Season

## Slide 10: SWPPP-Contents
Standards for Construction Activities
Background project info
Site Map
Soil Description
Construction Phasing Plan
Pollution Prevention Measures
Description of Construction and Waste Materials
Temporary and Permanent Structural and Vegetative Measures

## Slide 11: SWPPP-Contents (contents)
Map showing control measures
Details of control measures
Identify temporary measures to be converted to permanent control measures
Maintenance Schedule
Name of receiving water
Description of structural practices used to divert flows
Description of existing data that describes the stormwater runoff characteristics at the site

## Slide 12: Commonly Used SWPPP Measures
Construction Entrance
Mulching/Seeding
Silt Fences
Straw Bale Dikes
Drop Inlet Protection
Stone Check Dams
Prefabricated Check Dams

## Slide 13: Construction Entrance
http://www.harfordcountymd.gov/dpw/eng&const/WaterResources/Images/Sedimentcont2.jpg
http://pasture.ecn.purdue.edu/~sedspec/sedspec/images/construction.jpg

## Slide 14: Erosion Control (Mulching/Seeding)
http://www.terra-mulch.com/photos/11-11.JPG
http://www.ssseeds.com/ecb/photos/WS05/images/WS05%202-1%20Over%20Mulch.jpg

## Slide 15: Silt fences
www.acfenvironmental.com/ bmp_siltfence.htm
www.forestry.state.ar.us/ bmp/appn_soil.html

## Slide 16: Straw Bale Dikes
http://www.salmonhabitat.org/images/v3f52b.gif
http://www.forester.net/images/ec_0103_p78_top.jpg

## Slide 17: Drop Inlet Protection
http://unix.eng.ua.edu/~rpitt/Class/Erosioncontrol/Module8/Module8_files/image050.gif
http://www.greatamericantec.com/images/inlet.jpg

## Slide 18: From “Blue” Book

## Slide 19: Blue Book—Storm Drain Inlet Protection
Type I Excavated Drop Inlet Protection
Type II Fabric Drop Inlet Protection
Type III Stone & Block Drop Inlet Protection
Type IV Curb Drop Inlet Protection

## Slide 20: Blue Book—Type I Excavated Drop Inlet Protection

## Slide 21: Blue Book— Type II Fabric Drop Inlet Protection

## Slide 22: Blue Book— Type III Stone & Block Drop Inlet Protection-1

## Slide 23: Blue Book— Type III Stone & Block Drop Inlet Protection-2

## Slide 24: Blue Book— Type III Stone & Block Drop Inlet Protection-3

## Slide 25: Stone Check Dams
http://www.ncc-swnpdes.com/images/stone_creek_dam.jpg
http://www.dfr.state.nc.us/images/wq/glossary/rockcheckdam.jpg

## Slide 26: Other Check Dams
http://www.wsdot.wa.gov/NR/rdonlyres/BA478915-1B80-4188-BB59-37358244CBDF/0/CheckDam_Jan05.jpg
http://www.lakemac.infohunt.nsw.gov.au/erosion/images/09051.gif

## Slide 27: Site Plan/Inspection Report
Shows erosion control measures in relation to site
Indicates areas that need permanent measures
Indicates other action items based on inspection

## Slide 28: SPEDES Site Plan Example