## Slide 1: TR-55 Urban Hydrology for Small Watersheds

## Slide 2: Simplified methods for estimating runoff and peak discharge for small urban/urbanizing watersheds
Ch 1 Intro
Ch 2 Estimating Runoff
Ch 3 Time of Concentration
Ch 4 Peak Runoff Method
Ch 5 Hydrograph Method
Ch 6 Storage Volumes for Detention Basins

## Slide 3: Chapter 5 Tabular Hydrograph Method
Can be used to estimate runoff from nonhomogenous watersheds
Input:
  Same as Chapter 4 for each subarea
  Tt-travel time for each routing reach

## Slide 4: Steps
Use Worksheet 5a to calculate/summarize info on each subarea
Use worksheet 5b to route the various subareas

## Slide 5: Limitations
Accuracy decreases as complexity increases
Accuracy (+/- 25%)
Where possible, compare to gaged data
TR-20 (not TR-55) should be used if:
  Tt > 3hours
  Tc for any subarea > 2 hours
  Drainage areas differ by a factor of 5 or more
  Entire hydrograph is needed for detailed flood routings
  Peak discharge time must be determined accurately

## Slide 6
Subareas 1 & 2 routed through 3,5 and 7
Subareas 3 & 4 routed through 5 & 7
Subareas 5 & 6 routed through 7
Proposed subdivision in 5, 6 and 7

## Slide 7
Table 5-1 Initial abstraction as a function of curve number
Ia/P values are then calculated

## Slide 8
Exhibit 5 tables (4 different exhibits based on the 4 rainfall distribution types)
Prerouted using ATT-KIN method
Tables give unit peak discharge (multiply by DA and Q to get Discharge)
Ia/P values are rounded off to the nearest 0.1, 0.3 or 0.5 (or interpolated)
Travel time must be rounded off to table values

## Slide 13: Impact of Development
Peak flow is higher after development
Peak flow occurs earlier after development

## Slide 14: Low Impact Development
http://www.epa.gov/nps/lid/
http://www.lowimpactdevelopment.org/
http://www.lid-stormwater.net/

## Slide 15: Green Roofs

## Slide 16: Permeable/Porous Concrete Pavers
http://www.concretenetwork.com/concrete/porous_concrete_pavers/

## Slide 17: Pervious Pavements in Cold Weather

## Slide 18: Rain Gardens

## Slide 19: Grass Swales

## Slide 20: Detention/Retention Basins

## Slide 21: Break

## Slide 22: Ch 6 Estimating Storage Volumes for Detention Basins
Approximate method (+/-25% storage error)
Can be used for single and multi-staged outflow structures
Worksheet 6a-estimate storage volume given desired peak outflow
Worksheet 6b-estimate peak outflow given storage volume

## Slide 23: Detention Outlet Structures
Single Stage (culvert or orifice)
Multi-Staged to handle different flows
Combination of orifices &/or weirs

## Slide 24: Orifices and Weirs

## Slide 25: Figure 6-1 Approximate Routing

## Slide 26: Example 6-1 Single-Stage Outflow
75-Acre Development
Developed Peak flow is 360 cfs (Q25)
Present channel can handle only 180 cfs w/o significant damage
Storage-elevation curve is given-see worksheet
Determine storage volume of a detention basin
Assuming a rectangular weir, determine the weir length needed to limit the flow to 180 cfs

## Slide 27: Worksheet 6A

## Slide 28: Determining weir length (don’t need to do for class; covered in CTC 261)
Flow=3.2*Weir Length*(Weir Head)1.5
180=3.2*Weir Length*(5.7) 1.5
Weir Length=4.1 feet
Notes:
  Weir head=max. storage elevation-crest elev.
  A weir length greater than 4.1 feet would let more than 180 cfs into the drainage channel

## Slide 29: Example 6-3
10-Acre Development
Existing peak flow is 35 cfs
Developed peak flow is 42 cfs (24-hr, Q100)
Detention basin volume is 35,000 cubic feet
Estimate peak outflow

## Slide 30: Worksheet 6B