## Slide 1: Time of Concentration

## Slide 2: Objectives
Know how to calculate time of concentration
Know why it’s important to be able to determine the time of concentration

## Slide 3: Definition
Time required for runoff to travel from the hydraulically most distant point on a watershed to another point of interest within the watershed

## Slide 4: Factors
Surface roughness
Channel shape and flow patterns
Slope
Urbanization generally increases the runoff velocities and therefore decreases the time of concentration

## Slide 5: Importance
Rational method
  Calculate time of concentration, tc
  Set storm duration = tc
  Use IDF curve to find rainfall intensity
TR-55 Method
  Calculate time of concentration, tc
  Look up unit peak discharge on the appropriate Exhibit 4-#

## Slide 6: Typical Values for Tc < 50 Acres
5 minutes to 30 minutes

## Slide 7: Water can move through a watershed as:
Sheet flow (max of 300 ft; ---usually 100 ft)
Shallow concentrated flow
Open channel flow
  Gutter
  Ditch
  Swale
  Creek
All three or some combination

## Slide 8: Examples
Urban
  Sheet flow from back end of a residential lot
  Open channel flow once water drops over the curb and into a gutter
Rural
  Sheet flow in upper part of watershed
  Shallow concentrated flow as water forms rivulets
  Open channel flow (ditch/creek)

## Slide 9: Calculating Tc
Calculate Tc for each type of flow and add together
See the following TR-55 worksheet to be used for all Tc calculations in this class!!

## Slide 10: TR-55 Worksheet 3

## Slide 11: Sheet Flow
Manning’s Kinematic Solution
  See TR-55, pg 3-3 & equation 3-3
Kinematic Wave Equation
FAA Method
Nomograph
  Refer to https://www.roanokecountyva.gov/DocumentCenter/View/209/Chapter_4_Hydrology (pg 11)
  IN CLASS (use #1)

## Slide 12: 1-Manning’s Kinematic Solution
Tt=[0.007(nL).8]/[P2.5 S.4]
Tt is travel time (hrs)
n-Manning’s coefficient for sheet flow (dimensionless - must use Table 3-1 in TR-55)
L is flow length (ft)
P2 is 2-yr, 24-hr rainfall (in)
  TR-55 Appendix B, Figure B-3 or
  Local IDF curve (change intensity to inches)
S is slope (decimal format)

## Slide 13: 2-Kinematic Wave Equation (NYSDOT)
tco=[56(Lo).6 (n).6]/[So.3 i.4]
tco is travel time (sec)
n-Manning’s coefficient (dimensionless)
Lo is overland flow length (ft)
i is rainfall intensity for a desired frequency (in/hr)
  TR-55 Appendix B (change inches to intensity) or
  Local IDF curve
So is overland slope (decimal format)

## Slide 14: Nomograph for Sheet Flow

## Slide 15: Kinematic Wave Equation
Includes the rainfall intensity for a desired frequency
Must use iterative approach
  Assume a rainfall intensity
  Calculate travel time
  Set storm duration = travel time
  Look up intensity from IDF curve and compare to assumed value
  If intensity differs go back to step 1

## Slide 16: 3-FAA Equation
t=[1.8(1.1-C)(Lo).5 ]/[S.333]
t is travel time (min)
C-rational coefficient (dimensionless)
  See Appendix C-1 of your book
Lo is overland flow length (ft)
So is overland slope (decimal format)

## Slide 17: 4-Nomograph
Length
Ground character
  Paved
  Bare soil
  Poor/Avg/Dense Grass
Percent slope
http://sanantonio-tx.elaws.us/code/udc_apxh_ch5_5.4_sec5.4.1

## Slide 18: Example
Dense Grass (n=0.24, C=0.2)
Flow Length (200 ft)
Location (SUNY Poly; 2-yr 24-hr duration)
Slope (3%)

## Slide 19: Example: Manning’s Kinematic Solution
Tt=[0.007(nL).8]/[P2.5 S.4]
Tt=[0.007(.24*200).8]/[2.5.5*.03 .4]
n=.24
L=200 ft
P2 = 2.5 in (TR-55; Figure B-3)
S = .03
Tt=0.398 hours = 24 minutes

## Slide 20: Example: Kinematic Wave Equation
tco=[56(Lo).6 (n).6]/[So.3 i.4]
Assume 1-hr; 2-yr frequency (i=1”/hr)
tco=[56(200).6 (.24).6]/[.03.3*1.4]
tco=1640 seconds = 27 minutes
Intensity for 30-min; 2-yr storm =1.6”/hr
Intensities don’t match; try again

## Slide 21: Kinematic Wave- IDF Curve is needed

## Slide 22: Kinematic Wave-Trial/Error (Tc=9 minutes)
Assumed I | Time of Conc. | Actual i
1 in/hr | 28 minutes | 1.6 in/hr
1.6 | 17 | 2.4
2.4 | 11 | 3.1
3.1 | 9 | 3.1

## Slide 23: Example: FAA Equation
t=[1.8(1.1-C)(Lo).5 ]/[S.333]
t=[1.8(1.1-.2)(200).5 ]/[.03.333]
C=.2
Lo=200 ft
So = .03
t = 41 min

## Slide 24: Example: Nomograph
From nomograph C-2
Concentration time = 21 minutes
  Length=200 ft
  Dense Grass
  Slope=3%
  Note: had to extend pivot line

## Slide 25: Example Results
Manning’s Kinematic
Kinematic Wave
FAA
Nomograph
24 minutes
9 minutes
41 minutes
21 minutes

## Slide 26: Shallow Concentrated Flow
TR-55
  page 3-2; Figure 3-1
  page 3-3; Explanation
  Appendix F - formulas
Derived from Manning’s equation
Determine average velocity (Fig 3-1)
Divide flow length by average velocity to obtain travel time

## Slide 27: TR-55 Figure 3-1

## Slide 28: Shallow Concentrated Flow
Equations
  Velocity=16.1345*S0.5 Unpaved
  Velocity=20.8282*S0.5 Paved
Assumptions
  Unpaved: n=.05; hydraulic radius=0.4
  Paved: n=.025; hydraulic radius=0.2

## Slide 29: Document Work using TR-55 Worksheet 3

## Slide 30: Example Worksheet 3

## Slide 31: Questions
What is the definition of “time of concentration”
Name the 3 types of watershed flow?
What form do you use for tc calculation in this class?
Length/velocity results in what unit?

## Slide 32: Break
We covered time of concentration for:
sheet flow (A-B)
shallow concentrated flow (B-C)
Next—Time of Concentration for open Channel Flow (C-D)
Remember-always use TR-55 Worksheet 3 for documentation

## Slide 33: Open Channel Flow
Manning’s Equation (TR-55, page 3-4)
Calculate average velocity
Divide flow length by average velocity to obtain travel time
How do we determine “velocity”?

## Slide 34: Manning’s Equation
Irish Engineer
“On the Flow of Water in Open Channels and Pipes” 1891
Empirical equation
History: http://manning.sdsu.edu/\

## Slide 35: Uniform Flow in Open Channels
Water depth, flow area, discharge and velocity distribution at all sections throughout the entire channel reach remains unchanged.
The energy grade line, water surface line, and the channel bottom lines are all parallel to each other
No acceleration (or deceleration)

## Slide 36: Manning’s Equation: Flow---English
Q=A(1.49/n)(Rh2/3)(S).5
Q is flow rate (cfs)
n-Manning’s coefficient (dimensionless)
Rh is hydraulic radius (ft)
  Wetted area / wetted perimeter
S is slope (decimal format)

## Slide 37: Manning’s Equation: Flow---Metric
Q=A(1/n)(Rh2/3)(S).5
Q is flow rate (cms)
n-Manning’s coefficient (dimensionless)
Rh is hydraulic radius (m)
  Wetted area / wetted perimeter
S is slope (decimal format)

## Slide 38: Manning’s Equation: Velocity----English
Divide both sides by area
V=(1.49/n)(Rh2/3)(S).5
V is velocity (fps)
n-Manning’s coefficient (dimensionless)
Rh is hydraulic radius (ft)
  Wetted area / wetted perimeter
S is slope (decimal format)

## Slide 39: Manning’s Equation: Velocity-----Metric
V=(1/n)(Rh2/3)(S).5
V is velocity (meter/sec)
n-Manning’s coefficient (dimensionless)
Rh is hydraulic radius (m)
  Wetted area / wetted perimeter
S is slope (decimal format)

## Slide 40: Manning’s Coefficient Typical Values
Flowmaster
Another Reference:
  http://www.lmnoeng.com/manningn.htm

## Slide 41: Hydraulic Radius
Wetted area / wetted perimeter
Easy to calculate for circular pipes full or half-full, and use trig to calculate triangular or trapezoidal channels
Easiest to use software (Bentley flowmaster)

## Slide 42: SCS (now NRCS) Channel Calculations

## Slide 43: Example-Find V
Find the velocity of a rectangular channel 5’ wide w/ a 5% grade, flowing 1’ deep. The channel has a stone and weed bank (n=.035).
    A=5 sf; WP=7’; Rh=0.714 ft
    S=.05
    V=7.6 fps

## Slide 44: Example-Find time
If velocity = 7.6 ft per second and length of channel = 500 feet then time traveled in channel =l/v=500/7.6=
Time traveled=66 seconds = 1.1 minutes

## Slide 45: Flowmaster
Use flowmaster to solve previous example.
Note: The depth is unknown because you are in the process of trying to find the peak flow, so assume 1 foot or 1 meter. The velocity is not usually sensitive to the depth.

## Slide 46: Time of Concentration Calculations
For this class (homework, projects, etc.) use worksheet 3 from the TR-55 Document
Page D-3 (to print out blank form)
Also show picture of lengths and include flowmaster report

## Slide 47: Notes on Manning’s n for Worksheet 3
For sheet flow use n on Table 3-1.
For channel flow use typical n values for open channels.
See worksheet –next slide

## Slide 48: TR-55 Worksheet 3 Image

## Slide 49: Flowmaster software availability
Can use flowmaster for Manning’s equation (channel flow)
Labs 1159/G143 or download on your own computer
Click on Bentley folder, Click on Flowmaster; On left use trapezoidal channel

## Slide 50: Introduce Project 2
Simplified Stormwater Design

## Slide 51: Next Lecture
Rational Method for Determining Peak Flow