## Slide 1: Watersheds

## Slide 2: Outcomes
Read a contour map
Delineate a watershed
Determine slopes/lengths
Determine a drainage area

## Slide 3: We All Live in a Watershed
When water runs off your property where does it go?

## Slide 4: Importance of Watershed Protection
Pollutants can enter waterbodies
  Silt from construction sites, farms, erosion
  Septic system waste
  Fertilizers, pesticides
  Road salt
  Other pollutants (industry/commercial)

## Slide 5: Watershed Protection
SPDES (stormwater pollution discharge and elimination system)
Watershed action plans
Public Involvement (stewardship)

## Slide 6: Watershed Delineation
Any particular point on a water channel (stream, ditch, gutter, etc.) has an associated watershed area
The boundaries of a watershed are ridge lines (high points)
You can identify ridge lines by contour lines on topographic maps

## Slide 7: Contour Maps-Lines showing constant elevation

## Slide 8: 2d model of 3d surface

## Slide 9: Hints for reading contour maps
Flow paths are perpendicular to contour lines (why?)
Streams---Contour lines are concave (think V’s)
Ridges----Contour lines are convex (think noses)
Peaks of mountains and depressions (swamps, ponds) usually show as small circular areas
Contour lines close together indicate steep slopes (why?)
Contour lines which are far apart indicate flat slopes (why?)
Highlight rivers/creeks to your point of interest (it also sometimes helps to highlight them outside your point of interest)
Ignore roads; ideally, any construction project shouldn’t shift water to another watershed

## Slide 10: Steps-Delineating Drainage Areas
Identify your point of interest
Identify the channels/subchannels (V’s)
Identify the hill tops (circles)
Draw from hill-top to hill-top along the ridges (noses)

## Slide 11: Delineate Watershed
Class Demonstration (see next slide)

## Slide 12: Watershed Delineation using USGS Map

## Slide 13: Sub-Drainage Areas
Drainage areas may be broken up into sub-catchments (or sub-drainage) areas because:
  Drainage areas are usually modeled as homogeneous systems
  Streams are branched
  Points of interest need to be isolated

## Slide 14: Delineate Subareas
Handouts:
Delineating subareas for each reach

## Slide 15: Break

## Slide 16: Determining Drainage Areas
Stripping Method
Grid Method
Planimeter
Software Programs (GIS, Streamstats)

## Slide 17: Stripping/Grid Methods Scale is important!
http://www.globalsecurity.org/military/library/policy/army/fm/5-430-00-1/fig6-13.gif

## Slide 18: Planimeter

## Slide 19: Software
http://gis.esri.com/library/userconf/proc99/proceed/papers/pap676/p6764.gif

## Slide 20: Determining Stream Lengths
20
Edge of Paper Tic Method
String Method (non-stretch string)
Don’t use “as the crow flies”
Check scale (1”=2000’ or other)

## Slide 21: Data Collection
Land Use
Soil Characteristics
Slope (overland and channel)
Channel/Overland flow lengths
% Impervious
Channel cross-sections
Roughness characteristics
Storage (ponds, swamps, wetlands)

## Slide 22: Sources
Field reconnaisance
Aerial Photographs
NRCS Soil Maps
USGS Maps/Other Contour Maps
Planimetric mapping
Historical engineering studies
Survey Data
Soil Boring Data

## Slide 23: Common Conversions
1 acre = 43,560 ft2
1mi2 = 640 acres
1 hectare = (100 m)2 = 10,000 m2
1 acre = 0.405 hectare
1 hectare = 2.46 acres
1 meter = 3.2808 feet
1 foot = 0.3045 meter

## Slide 24: Downloading USGS Maps *.pdf
https://www.usgs.gov/programs/national-geospatial-program/topographic-maps

## Slide 25: Other tools:
Image capture software:
  Snipping Tool (on engineering computers)
  In adobe reader use tools, select and zoom, snapshot tool, to capture images
USGS pdf’s---click on images, click off orthoimages to turn off the background photogrammetry

## Slide 26: Streamstats
https://water.usgs.gov/osw/streamstats/
https://streamstats.usgs.gov/ss/

## Slide 27: Other Sources
NRCS pdf – determining watershed
https://www.epa.gov/waterdata/hows-my-waterway
Watersheds - NYDEC

## Slide 28: Next Lecture
Precipitation
  Definition
  What affects it?
  Return period
  Probability of an event occurring over a time interval
  Design Frequencies
  IDF Curves