## Slide 1: CTC 261 Culvert Basics

## Slide 2: Objectives
Students should have the ability to:
Describe the different materials used for culverts
Describe inlet and outlet control
Determine the headwater depth for inlet control

## Slide 3: Hydraulic Design of Highway Culverts
USDOT/FHWA
HDS 5 (highway design series #5)
HDS 5 (2005/2012 versions) available at:
https://people.sunypoly.edu/~barans/classes/ctc261/lectures.html
Most of the images in this powerpoint presentation were taken from HDS 5

## Slide 4: Culvert
Hydraulically short conduit which conveys stream flow through a roadway embankment or past some other type of flow obstruction

## Slide 5: Culvert Design
Conduit placed under a road to carry water from one side to the other
Designed to pass a design flow w/o overtopping the road

## Slide 6: Culvert Flow
Complex
  Pressure flow
  Open channel flow
  Combination
Variables
  Slope
  Pipe Diameter, Length and Roughness
  Entrance Design
  Exit Design

## Slide 7: Culvert Shapes

## Slide 8: Culvert Materials

## Slide 9: Culvert Materials-other
Corrugated Aluminum
Plastic
  Polyethylene
  Polyvinylchloride (PVC)
Stone

## Slide 10: Inlet Types

## Slide 11: Culvert Hydraulics
Complete theoretical analysis is difficult
Flow conditions vary from culvert to culvert
Flow conditions vary over time
May flow full or partly full
Flow control-inlet or outlet
HDS approach is to analyze culvert for both types of flow control and design for minimum performance

## Slide 12: Flow Conditions
Full Flow (pressure) – rare
Partly Full (free surface) Flow
  Subcritical
  Critical
  Supercritical
Evaluate flow regime via Froude #
  Fr<1 Subcritical – Smooth flow, tranquil, low velocities
  Fr=1 Critical Flow (point of minimum specific energy)
  Fr>1 Supercritical – Swift, rapid, high velocities

## Slide 13: Headwater (HW)
Depth of upstream water surface measured from invert of culvert entrance
  Should not exceed edge of shoulder elevation (account for freeboard)
  Should not be so high as to cause flooding problems

## Slide 14: Headwater (HWo)
Depth of upstream water surface measured from invert of culvert outlet

## Slide 15: Tailwater (TW)
Depth of downstream water surface measured from invert of culvert outlet
  Usually determined by backwater calc’s.
  Sometimes (and for this class) determined by normal depth calculations

## Slide 16: Outlet Velocity
Outlet velocities are usually higher than in natural channel (constriction)
High velocities can cause streambed scour and bank erosion

## Slide 17: Performance Curves
Plot of HW depth or elevation versus flow rate
  Inlet control curves
  Outlet control curves

## Slide 18: Economics
Risk:
Decreases w/ larger culvert
Cost:
Increases w/ larger culvert
Usually use a Design Frequency

## Slide 19: Inlet Control
Inlet controls (or limits) the flow
Harder for flow to get through the entrance of the culvert than it is to flow through the remainder of the culvert

## Slide 20: Inlet Control –A
Barrel flow is partly full and supercritical (below critical depth)
Critical depth occurs just d/s of culvert entrance
Flow approaches normal depth @ outlet end

## Slide 21: Inlet Control –B
Flow d/s of inlet is supercritical (below critical depth)
Hydraulic jump occurs in the barrel
Note that submergence of outlet does not assure outlet control

## Slide 22: Inlet Control –C
Barrel flow is partly full and supercritical (below critical depth)
Critical depth occurs just d/s of culvert entrance
Flow approaches normal depth @ outlet end

## Slide 23: Inlet Control –D (rare)
Median drain provides ventilation/stable conditions
Hydraulic jump occurs in the barrel
Note that full-flow doesn’t occur even though inlet/outlet are submerged

## Slide 24: Increasing inlet performance Beveled edges at entrance

## Slide 25: Increasing inlet performance Square Edges/Curved Edges

## Slide 26: Fall-Depressing the culvert entrance below the natural stream bed

## Slide 27: Tapered Entrances

## Slide 28: Outlet Control
Outlet controls (or limits) the flow
Harder for flow to negotiate length of culvert than it is to get through the inlet (entrance)

## Slide 29: Outlet Control –A (rare)
Pressure Flow
Full Flow
Most culverts don’t operate this way
Inlet/Outlet Submerged

## Slide 30: Outlet Control –B
Full Flow
Inlet not fully submerged

## Slide 31: Outlet Control –C
Submerged inlet / unsubmerged outlet
Requires high HW
Outlet velocities usually high

## Slide 32: Outlet Control –D (Typical)
Inlet submerged
Outlet unsubmerged
Critical depth occurs just u/s of outlet
Low TW

## Slide 33: Outlet Control –E (typical)
Flow is subcritical (laminar)
Inlet and outlet are unsubmerged

## Slide 34: Break

## Slide 35: Factors that Influence Inlet/Outlet Control

## Slide 36: Data Requirements-Hydrology
Peak Flow
Check Flow
Hydrograph
  Storage routing
Stream gage/regression/rational method/TR-55
Same as above
Stream gage/ synthetic methods

## Slide 37: Data Requirements Site Data
Culvert Location
Waterway Data
  Cross Sections
  Long. Slope
  Resistance
Roadway Data
  Cross Section
  Profile
  Culvert Length
Maps
Field Surveys
Roadway Plans

## Slide 38: Data Requirements Design Headwater
  Critical pts
  Surrounding bldgs
  Regulatory Constraints
  Arbitrary Constraints
Roadway plans
Maps/plans/photos
Floodplain/flood insurance regs
State or local regs

## Slide 39: Inlet Hydraulics
Entrance Unsubmerged (weir)
Entrance Submerged (orifice)
Transition (in between; poorly defined)

## Slide 40: Weir and Orifice Flow Equations

## Slide 41: Hydraulics-Energy Equation (EGL)
HW and TW depths and elevations
Velocity head (u/s & d/s)
Head losses
  Friction loss through the barrel
  Entrance/Exit losses
  Bend/Junction/Grate losses

## Slide 42: Energy and Hydraulic Grade Lines

## Slide 43: Definitions: Head (Friction) Losses
He-entrance loss
Hf-friction loss through the barrel
Ho-exit loss
Other potential losses due to bends, junctions and grates
Summarize the losses to calculate the total energy required to “push” water through the barrel

## Slide 44: Definitions: Velocity
Vu-channel velocity upstream of the culvert
V-velocity through culvert barrel
Vd-channel velocity downstream of the culvert
Vu/Vd are often assumed to be minimal and left out of the equations

## Slide 45: Roadway Overtopping

## Slide 46: Modeling Roadway Topping
Water flows through the culvert
Water also flows over the road – model as a broad crested weir
Topping usually occurs on sag curve
  Represent sag w/ a single horizontal line
  Represent sag w/ a series of lines

## Slide 47: Culvert Design Form
Page 344 of HDS-5
Calculate HW elev based on inlet/outlet control

## Slide 48: Culvert Design Form-Use for Class

## Slide 49: Culvert Design Steps
Summarize all known data
Select a preliminary culvert material, shape, size and entrance type
Perform inlet control calculations
Perform outlet control calculations
If HW elevation is too high, then go back to step 2

## Slide 50: Inlet Control
First step is to determine HW/D from charts
  Chart 1B (Concrete Pipe-English)
  Chart 2B (Corrugated Metal Pipe-English)
  Chart 3B (Circular Pipe-Beveled Ring)
  Chart 8B (Box Culverts) –D is box culvert Ht
  Note: Must calculate Q per foot of culvert box width
Multiply by Diameter or Box Culvert Height to get HW

## Slide 51: HW versus different ends
Dia=42” (3.5)
Q=120 cfs
Square edge with headwall
  HW/D=2.5
  HW=8.8’
Groove end with headwall
  HW/D=2.1
  HW=7.4’
Groove end projecting
  HW/D=2.2
  HW=7.7’

## Slide 52: First Homework
Show only inlet control calculations.
Read and use HDS-5
Use the culvert form from HDS-5 (2005)-larger-page 344
For CBC calculate Q/width of box

## Slide 53: Next Lecture
Culvert Design Form Outlet control