## Slide 1: Culvert Hydraulics using the Culvert Design Form

## Slide 2: Objectives
Know how to use the culvert design form to evaluate and size simple culverts (page 344 of 2005 HDS 5)

## Slide 3: Culvert Design Form

## Slide 4: Step 1
Summarize all known data and select a preliminary culvert size, shape and entrance type

## Slide 5: Step 2
Choose a culvert type and size

## Slide 6: Step 3-Inlet Control Calculations
Inlet control calculations
  Determine HW/D from Design Charts
  Calc HW depth
  Calc Fall (don’t do for this class)
  Calc the Elev of the HW for inlet control

## Slide 7: Step 4-Outlet Control Calculations
Outlet control calculations
  Determine TW depth
  Determine critical depth
  Find the average of critical depth and diameter
  Determine depth from culvert outlet invert to HGL
  Determine all head losses
  Calc the Elev of the HW for outlet control

## Slide 8: Step 5-Evaluate Results
Higher of the two elevations designates control
Choose larger culvert if the highest elevation is unacceptable

## Slide 9: Example Problem 1 (pg 56 of HDS5-2005)
Q25=200 cfs
Natural channel slope=1%
TW=3.5 ft
L=200 ft
Natl streambed elev. @ entrance = 100 ft
Shoulder Elev=110 ft (2-ft freeboard)
Evaluate 72” (6’) CMP (45 deg bevel)

## Slide 10: Culvert Design Form Data

## Slide 11: Step 2 Inlet Control Calculations
HW/D from Design Chart 3B = 0.96
HW=0.96*6’=5.8’
A =45 deg bevel, pg 27
B =33.7 deg bevel

## Slide 12: Step 3-Inlet Control Calculations Calculate Fall—Assume Fall=0 for this class
Max. Available HW depth = 108-100= 8’
Fall = Calc HW depth – Available HW depth
  5.8’-8’= -2.8 ft
  Fall is negative; therefore set fall = 0
  Note: If fall is + then the invert must be lowered to allow enough head to “push” desired Q through the culvert

## Slide 13: Step 3-Inlet Control Calculations Calculate HW Elev for inlet control
ELhi=HWi+ELi
5.8 ft+100 ft = 105.8 feet

## Slide 14: Step 4-Outlet Control Calculations TW Depth
  Determine TW depth
  Backwater calculations (not covered in this class) or find normal depth using Manning’s equation (or Flowmaster)
  Given as 3.5’

## Slide 15: Step 4-Outlet Control Calculations Critical Depth in Culvert (could also use flowmaster)
  Determine Critical Depth (Chart 4A) 3.8’

## Slide 16: Step 4-Outlet Control Calculations Find average of dc + D
(3.8+6)/2 = 4.9’
Average of critical depth and diameter of pipe

## Slide 17: Step 4-Outlet Control Calculations Determine ho
  ho is the depth from the culvert outlet invert to the hydraulic grade line
  Larger of:
    TW (3.5’) or
    Avg. of (dc & D-4.9’) ---See Figure III-9 (D)

## Slide 18: Step 4-Outlet Control Calculations Find Entrance Loss Coefficient, Ke
  Ke= 0.2

## Slide 19: Outlet Control Head Losses
  Can use Chart 6
  Line D/Ke
  Line Q/Turning Pt
  H=2.6’

## Slide 20: Step 4-Outlet Control Calculations Calculate HW Elevation
  Outlet Invert Elev + Head Losses + ho
  98+2.6+4.9
  HW elevation based on outlet control = 105.5’

## Slide 21: Step 5 Evaluate Results
Culvert is operating under inlet control 105.8
There is still 2 ft of head available (compare to 108)
Try a smaller culvert

## Slide 22: Outlet Velocity – Inlet Control (pg 50)
  Velocity at normal depth (in the culvert barrel) is assumed to be the outlet velocity
  Use Manning’s equation (by hand or using Flowmaster and solve for normal depth)
    Calculate depth which gives a Q of 200 cfs
    Velocity = 9.2 cfs

## Slide 23: Outlet Velocity- Outlet Control page 50
Use critical depth if TW<critical depth
Use TW if TW is between critical depth and top of barrel
Use full depth of barrel if TW is above top of barrel

## Slide 24: Culvert Design (Allowable HW is 108.0’)

## Slide 25: Culvert Master (Quick Calculator)

## Slide 26: Culvert Design
Multiple structures
  For 2 pipes or boxes of same size, etc. determine Q/2 and evaluate 1 pipe (or box)
For concrete box culvert
  6’ x 5’ (span x height)
  Q/H = Flow per foot of span
  D = height of culvert box (5’)

## Slide 27: Break

## Slide 28: Chapter VI – Special Considerations Flow Control & Measurement
Irrigation Canals
Stormwater Management Ponds
Cooling Waterchannels
Use routing to determine inflow into any pond upstream of culvert

## Slide 29: Chapter VI – Special Considerations Low Head Installations
Convey water under a roadway w/ min. HW and energy loss
Usually found in irrigation systems
Sag culverts sometimes used

## Slide 30: Chapter VI – Special Considerations Bends – Horizontal or Vertical

## Slide 31: Chapter VI – Special Considerations Junctions

## Slide 32: Chapter VI – Special Considerations Siphons (vacuum)-rarely designed

## Slide 33: Chapter VI – Special Considerations Fish Passage