## Slide 1: Final Review
Manning’s Equation (Uniform Flow)
  Normal Depth
Varied Flow
  Specific Energy
  Critical Depth
  Froude Number
Culvert Design
  Inlet and Outlet Control Flow Types
  Culvert Design Worksheet (worst case Headwater)
  Velocity at Exit

## Slide 2: Orifices/Weirs
Be able to solve orifice and weir problems

## Slide 3: Uniform Flow in Open Channels
Water depth, flow area, Q and V distribution at all sections throughout the entire channel reach remains unchanged
The EGL, HGL and channel bottom lines are parallel to each other
No acceleration or deceleration

## Slide 4: Manning’s Equation-English Solve for Flow
Q=AV=(1.486/n)(A)(Rh)2/3S1/2
Where:
Q=flow rate (cfs)
A=wetted cross-sectional area (ft2)
Rh=hydraulic radius=A/WP (ft)
WP=wetted perimeter (ft)
S=slope (ft/ft)
n=friction coefficient (dimensionless)

## Slide 5: Normal Depth
Given Q, the depth at which the water flows uniformly
Use Manning’s equation
  Must solve by trial/error (depth is in area term and in hydraulic radius term)

## Slide 6: Normal Depth Example
Find normal depth in a 10.0-ft wide concrete rectangular channel having a slope of 0.015 ft/ft and carrying a flow of 400 cfs.
Assume:
  n=0.013

## Slide 7: Normal Depth Example-Table
Assumed D (ft) | Area (sqft) | Peri. (ft) | Rh (ft) | Rh^.66 | Q (cfs)
2.00 | 20 | 14 | 1.43 | 1.27 | 356
3.00 | 30 | 16 | 1.88 | 1.52 | 640
2.15 | 21.5 | 14.3 | 1.50 | 1.31 | 396

## Slide 8: Specific Energy
Energy above channel bottom
  Depth of stream
  Velocity head

## Slide 9: Depth as a function of Specific Energy
Rectangular channel
  Width is 6’
  Constant flow of 20 cfs

## Slide 12: Critical Depth
Depth at which specific energy is at a minimum
Other than critical depth, specific energy can occur at 2 different depths
  Subcritical (tranquil) flow d > dc
  Supercritical (rapid) flow d < dc

## Slide 13: Calculating Critical Depth
A3/T=Q2/g
A=cross-sectional area (sq ft or sq m)
T=top width of channel (ft/m)
Q=flow rate (cfs or cms)
g=gravitational constant (32.2/9.81)
  Rectangular Channel—Solve Directly
  Other Channel Shape-Solve via trial & error

## Slide 14: Critical Depth (Rectangular Channel)
  Width of channel (T) does not vary with depth; therefore, critical depth (dc) can be solved for directly:
  dc=(Q2/(g*T2))1/3
  For all other channel shapes the top width varies with depth and the critical depth must be solved via trial and error (or via software like flowmaster)

## Slide 15: Froude Number
F=Vel/(g*D).5
F=Froude #
V=Velocity (fps or m/sec)
D=hydraulic depth=a/T (ft or m)
g=gravitational constant
  F=1 (critical flow)
  F<1 (subcritical; tranquil flow)
  F>1 (supercritical; rapid flow)

## Slide 16: Culvert Design
Should understand the following:
Headwater/Tailwater
Velocity (upstream/through culvert/downstream)
Slope/Size/Material/Inlet types
Use culvert design form

## Slide 18: Step 1
Summarize all known data and select a preliminary culvert size, shape and entrance type

## Slide 19: Step 2
Choose a culvert type and size

## Slide 20: Step 3-Inlet Control Calculations
Inlet control calculations
  Determine HW/D from Design Charts
  Calc HW depth
  Calc Fall (don’t use for this class)
  Calc the Elev of the HW for inlet control

## Slide 21: Step 4-Outlet Control Calculations
Outlet control calculations
  Determine TW depth
  Determine critical depth
  Find the average of critical depth and diameter
  Determine depth from culvert outlet invert to HGL
  Determine all head losses
  Calc the Elev of the HW for outlet control

## Slide 22: Step 5-Evaluate Results
Higher of the two elevations designates control
Calculate Downstream Velocity
Choose larger culvert if the highest elevation is unacceptable

## Slide 23: Outlet Velocity – Inlet Control
  Velocity at normal depth (in the culvert barrel) is assumed to be the outlet velocity
  Use Manning’s equation (by hand or using Flowmaster and solve for normal depth)

## Slide 24: Outlet Velocity- Outlet Control
Use critical depth if TW<critical depth
Use TW if TW is between critical depth and top of barrel
Use full depth of barrel if TW is above top of barrel

## Slide 25: Final Review
For the final use HDS-5 (2005) for inlet control types as shown on the following slides
HDS-5 (2012) has revisions and follows HY-8

## Slide 26: Inlet Control –A
Barrel flow is partly full and supercritical (below critical depth)
Critical depth occurs just d/s of culvert entrance
Flow approaches normal depth @ outlet end

## Slide 27: Inlet Control –B
Flow d/s of inlet is supercritical (below critical depth)
Hydraulic jump occurs in the barrel
Note that submergence of outlet does not assure outlet control

## Slide 28: Inlet Control –C
Barrel flow is partly full and supercritical (below critical depth)
Critical depth occurs just d/s of culvert entrance
Flow approaches normal depth @ outlet end

## Slide 29: Inlet Control –D (rare)
Median drain provides ventilation/stable conditions
Hydraulic jump occurs in the barrel
Note that full-flow doesn’t occur even though inlet/outlet are submerged

## Slide 30: Outlet Control –A (rare)
Pressure Flow
Full Flow
Most culverts don’t operate this way
Inlet/Outlet Submerged

## Slide 31: Outlet Control –B
Full Flow
Inlet not fully submerged

## Slide 32: Outlet Control –C
Submerged inlet / unsubmerged outlet
Requires high HW
Outlet velocities usually high

## Slide 33: Outlet Control –D (Typical)
Inlet submerged
Outlet unsubmerged
Critical depth occurs just u/s of outlet
Low TW

## Slide 34: Outlet Control –E (typical)
Flow is subcritical (laminar)
Inlet and outlet are unsubmerged