## Slide 1: CTC 261 Hydraulics Introduction
It’s no coincidence that a meter---not one-millionth of a meter and not ten thousand meters—is, roughly speaking, the size of a person. It’s about twice the size of a baby and half the size of a fully grown man. It would be rather strange to find that the basic unit we use for common measurements was one-hundredth the size of the Milky Way or the length of an ant’s leg.
Lisa Randall, Professor of Theoretical Physics, Harvard
Knocking on Heaven’s Door, 2011, ISBN 978-0-06-172372-8

## Slide 2: Class Requirements
On-Web: http://people.sunypoly.edu/~barans/
  Syllabus
  Schedule
  Lectures
  Grades
Brightspce
  Homework Assignments/Drop Boxes
  “Lab” Materials and Drop Boxes
Check prereq (224 or equiv)

## Slide 3: Objectives
Class requirements
Discuss the definition of hydraulics
Be familiar with common fluid properties

## Slide 4: Fluid Mechanics
Science that deals with the action of forces on fluids
Pratt’s Falls Park

## Slide 5: Fluid
Continuously deforms

## Slide 6: Hydrodynamics vs Gas Dynamics
Noncompressible
No change in density
Mathematically easier
Compressible
Significant density change
Mathematically more difficult

## Slide 7: Hydraulics
An extension of fluid mechanics in which many empirical relationships are applied and simplifying assumptions made to achieve practical engineering solutions

## Slide 8: Significance in Civil Engineering
Water systems
Wastewater systems
Open channel flow
Dams
Erosion Control
Hydraulic Structures
  Bridges
  Culverts
  Ditches
  Retaining structures

## Slide 9: History
5,000 years ago | Irrigation | Egypt
2,500 BC | Bamboo pipes | China
200 BC | Lead/Bronze Pipes | Rome
Romans built many stone aqueducts, many of which are still standing.
Utilization of theory began after 1850. Before that, designs were rule-of-thumb.

## Slide 10: Loss of Culvert
Loss of Culvert due to flooding on I-88
June 28,2006
Two truckers were killed

## Slide 11: Downstream View

## Slide 12: Collapse Culvert

## Slide 13: View after Culvert Loss

## Slide 14: Break

## Slide 15: Common Fluid Properties
 | SI | USC/FPS
Temperature | K (273+C) | F
Mass | Kg | Slug
Length | Meter (m) | Foot (ft)
Time | Second (sec) | Second (sec)
Force | N (kg-m/sec2) | Lb (slug-ft/sec2)
Pressure | Pascal (N/m2) | Psi

## Slide 16: Other common units
 | SI | USC/FPS
Gravity Constant | 9.81 m/sec2 | 32.2 ft/sec2
Specific Weight, Water (force per unit volume) | 9.81 kN/m3 (0-10 deg C) | 62.4 #/ft3 (40-60 deg F)
Mass Density, Water (mass per unit volume) | 1000 kg/m3 (0-10 deg C) | 1.94 slugs/ft3 (40-70 deg F)
Specific Gravity | Specific weight of a liquid / specific weight of water (at some std. temp.) | 

## Slide 17: Other common units
 | SI | USC/FPS
Kinematic Viscosity (area/time) | 1.31E-6 m2/sec 10 deg C | 1.22E-5 ft2/sec 60 deg F
Dynamic (Absolute) Viscosity (force-time/area) | 1.32E-3 N-sec/m2 (10 deg C) | 2.36E-5 #-sec/ft2 (60 deg F)
Kinematic Viscosity=Dynamic Viscosity/Density or Kinematic Viscosity*Density=Absolute Viscosity |  | 
https://www.cscscientific.com/csc-scientific-blog/whats-the-difference-between-dynamic-and-kinematic-viscosity

## Slide 18: Water Properties
Water properties are a function of temperature/pressure
See Brightspace, Content for the water properties table to be used in this class.

## Slide 19: Other Fluid Properties – Thermodynamics
Specific Heat (Joule per Kelvin-kg)
Specific Internal Energy (Joule per kg)
Specific Enthalpy (kJ/kg)

## Slide 20: Elasticity of Water
Amount of deformation for a given pressure change (bulk modulus of elasticity)
Water is essentially incompressible (although it is approximately 100 times more compressible than steel)
See http://hyperphysics.phy-astr.gsu.edu/hbase/permot3.html for equation relating to pressure and volume change

## Slide 21: Water Elasticity
What pressure is required to reduce the volume of water by 0.5% (.005)?
Using equation the pressure required is approximately 1,600 psi
(3/4 of a ton per square inch)

## Slide 22: Viscosity
Related to resistance of shear forces
Newtonian fluid: linear relationship between shear stress and the rate of deformation (gases and most liquids)
Non-Newtonian fluid: nonlinear relationship (thick, long-chained hydrocarbons)
High Viscosity: honey, tar
Low Viscosity: water, air

## Slide 23: Viscosity
For a Newtonian fluid
Shear stress(F/A)=Viscosity*Shear Rate
Shear rate (velocity gradient) is the rate at which one layer moves relative to an adjacent layer (change in velocity divided by change in distance)

## Slide 24: Newtonian vs Non-Newtonian

## Slide 25: Non-Newtonian Fluid
http://www.youtube.com/watch?v=cuzn8wh8Fys&feature=related

## Slide 26: Viscosity-Units
Dynamic (absolute)
  Units are N-sec/m2 or lb-sec/ft2
Kinematic
  Dynamic viscosity divided by mass density
  Units are m2/sec or ft2/sec

## Slide 27: Viscosity-Example
A Newtonian fluid is in the clearance between a shaft and a bearing. When a force of 600N is applied to the shaft parallel to the bearing sleeve, the shaft attains a speed of 1 m/s. If a 1500-N force is applied what speed will the shaft attain?

## Slide 28: Viscosity
For a Newtonian fluid
Shear stress(F/A)=Viscosity*Shear Rate
Answer:
Speed (sheer rate) would be proportional to the force since the area, viscosity and distance between bearing sleeve and shaft are constant. Therefore Speed =2.5 m/sec (1500/600)

## Slide 29: Brightspace-See HW assignment
Show students

## Slide 30: Next Lecture
Fluid Statics
  Absolute/gage pressure
  Hydrostatic pressure on horizontal surfaces
  Converting pressure to pressure head
  Defining center of pressure
  Hydrostatic pressure on vertical surfaces