## Slide 1: CTC 261 Review
Hydraulic Devices
  Orifices
  Weirs
  Sluice Gates
  Siphons
  Outlets for Detention Structures

## Slide 2: This Week:
Open Channel Flow
  Uniform Flow (Manning’s Equation)
  Varied Flow

## Slide 3: Objectives
Students should be able to:
Use Manning’s equation for uniform flow calculations
Calculate Normal Depth by hand
Calculate Critical Depth by hand
Utilize Flowmaster software for open channel flow problem-solving

## Slide 4: Open Channel Flow
Open to the atmosphere
  Creek/ditch/gutter/pipe flow
Uniform flow-EGL/HGL/Channel Slope are parallel
  velocity/depth constant
Varied flow-EGL/HGL/Channel Slope not parallel
  velocity/depth not constant

## Slide 5: Uniform Flow in Open Channels
Water depth, flow area, Q and V distribution at all sections throughout the entire channel reach remains unchanged
The EGL, HGL and channel bottom lines are parallel to each other
No acceleration or deceleration

## Slide 6: Manning’s Equation
Irish Engineer
“On the Flow of Water in Open Channels and Pipes” (1891)
More:
  http://www.engineeringtoolbox.com/mannings-roughness-d_799.html
  https://www.hydrologystudio.com/pulp-friction/
  https://www.h2ometrics.com/manning-equation/

## Slide 7: Manning’s Equation-English Solve for Flow
Q=AV=(1.486/n)(A)(Rh)2/3S1/2
Where:
Q=flow rate (cfs)
A=wetted cross-sectional area (ft2)
Rh=hydraulic radius=A/WP (ft)
WP=wetted perimeter (ft)
S=slope (ft/ft)
n=friction coefficient (dimensionless)

## Slide 8: Manning’s Equation-Metric Solve for Flow
Q=AV=(1/n)(A)(Rh)2/3S1/2
Where:
Q=flow rate (cms)
A=wetted cross-sectional area (m2)
Rh=hydraulic radius=A/WP (m)
WP=wetted perimeter (m)
S=slope (m/m)
n=friction coefficient (dimensionless)

## Slide 9: Manning’s Equation-English Solve for Velocity
V=(1.486/n)(Rh)2/3S1/2
Where:
V=velocity (ft/sec)
A=wetted cross-sectional area (ft2)
Rh=hydraulic radius=A/WP (ft)
WP=wetted perimeter (ft)
S=slope (ft/ft)
n=friction coefficient (dimensionless)

## Slide 10: Manning’s Equation-Metric Solve for Velocity
V=(1/n)(Rh)2/3S1/2
Where:
V=flow rate (meters/sec)
A=wetted cross-sectional area (m2)
Rh=hydraulic radius=A/WP (m)
WP=wetted perimeter (m)
S=slope (m/m)
n=friction coefficient (dimensionless)

## Slide 11: Manning’s Friction Coefficient
http://www.lmnoeng.com/manningn.htm
Typical values:
  Concrete pipe: n=.013
  CMP pipe: n=.024

## Slide 12: Triangular/Trapezoidal Channels
Must use trigonometry to determine area and wetted perimeters

## Slide 13: Pipe Flow
Hydraulic radii and wetted perimeters are easy to calculate if the pipe is flowing full or half-full
If pipe flow is at some other depth, then tables/figures/software are usually used

## Slide 14: SCS Table

## Slide 15: Example-Find Q
Find the discharge of a rectangular channel 5’ wide w/ a 5% grade, flowing 1’ deep. The channel has a stone and weed bank (n=.035).
A=5 sf; WP=7’; Rh=0.714 ft
S=.05
Q=38 cfs

## Slide 16: Example-Find S
A 3-m wide rectangular irrigation channel carries a discharge of 25.3 cms @ a uniform depth of 1.2m. Determine the slope of the channel if Manning’s n=.022
A=3.6 sm; WP=5.4m; Rh=0.667m
S=.041=4.1%

## Slide 17: Friction loss
How would you use Manning’s equation to estimate friction loss?

## Slide 18: Using Manning’s equation to estimate pipe size
Size pipe for Q=39 cfs
Assume full flow
Assume concrete pipe on a 2% grade
Put Rh and A in terms of Dia.
Solve for D=2.15 ft = 25.8”
Choose a 27” or 30” RCP

## Slide 19: Break

## Slide 20: Normal Depth
Given Q, the depth at which the water flows uniformly
Use Manning’s equation
  Must solve by trial/error (depth is in area term and in hydraulic radius term)

## Slide 21: Normal Depth Example
Find normal depth in a 10.0-ft wide concrete rectangular channel having a slope of 0.015 ft/ft and carrying a flow of 400 cfs.
Assume n=0.013 (concrete)

## Slide 22: Normal Depth Example Table
Assumed D (ft) | Area (sqft) | Peri. (ft) | Rh (ft) | Rh^.66 | Q (cfs)
2.00 | 20 | 14 | 1.43 | 1.27 | 356
3.00 | 30 | 16 | 1.88 | 1.52 | 640
2.15 | 21.5 | 14.3 | 1.50 | 1.31 | 396

## Slide 23: Stream Rating Curve
Plot of Q versus depth (or WSE)
Also called stage-discharge curve

## Slide 24: Specific Energy
Energy above channel bottom
  Depth of stream
  and
  Velocity head

## Slide 25: Depth as a function of Specific Energy
Rectangular channel
  Width is 6’
  Constant flow of 20 cfs

## Slide 26: Specific Energy: Table Derivision

## Slide 27: Specific Energy Curve

## Slide 28: Critical Depth
Depth at which specific energy is at a minimum
Other than critical depth, specific energy can occur at 2 different depths
  Subcritical (tranquil) flow d > dc
  Supercritical (rapid) flow d < dc

## Slide 29: Critical Velocity
Velocity at critical depth

## Slide 30: Critical Slope
Slope that causes normal depth to coincide w/ critical depth

## Slide 31: Calculating Critical Depth
a3/T=Q2/g
A=cross-sectional area (sq ft or sq m)
T=top width of channel (ft/m)
Q=flow rate (cfs or cms)
g=gravitational constant (32.2/9.81)
  Rectangular Channel—Solve Directly
  Other Channel Shape-Solve via trial & error

## Slide 32: Critical Depth (Rectangular Channel)
  Width of channel does not vary with depth; therefore, critical depth (dc) can be solved for directly:
  dc=(Q2/(g*w2))1/3
  For all other channel shapes the top width varies with depth and the critical depth must be solved via trial and error (or via software like flowmaster)

## Slide 33: Froude Number
F=Vel/(g*D).5
F=Froude #
V=Velocity (fps or m/sec)
D=hydraulic depth=a/T (ft or m)
g=gravitational constant
  F=1 (critical flow)
  F<1 (subcritical; tranquil flow)
  F>1 (supercritical; rapid flow)

## Slide 34: Varied Flow
Rapidly Varied – depth and velocity change rapidly over a short distance; can neglect friction
  hydraulic jump
Gradually varied – depth and velocity change over a long distance; must account for friction
  backwater curves

## Slide 35: Hydraulic Jump-Why
Occurs when water goes from supercritical to subcritical flow
Abrupt rise in the surface water
Increase in depth is always from below the critical depth to above the critical depth

## Slide 36: Hydraulic Jump-Details
Velocity and depth before jump (v1,y1)
Velocity and depth after jump (v2,y2)
Although not in your book, there are various equations that relate these variables. Specific energy lost in the jump can also be calculated.

## Slide 37: Hydraulic Jump-Example Links
http://krcproject.groups.et.byu.net/
http://www.lmnoeng.com/Channels/HydraulicJump.php
Circular hydraulic jump https://www.researchgate.net/figure/A-representative-circular-hydraulic-jump-formed-when-a-vertical-water-jet-impinges-on-a_fig1_338609088

## Slide 38: Varied Flow Slope Categories
M-mild slope
S-steep slope
C-critical slope
H-horizontal slope
A-adverse slope

## Slide 39: Varied Flow Zone Categories
Zone 1
  Actual depth is greater than normal and critical depth
Zone 2
  Actual depth is between normal and critical depth
Zone 3
  Actual depth is less than normal and critical depth

## Slide 40: Water-Surface Profile Classifications
H2, H3 (no H1)
M1, M2, M3
C1, C3 (no C2)
S1, S2, S3
A2, A3 (no A1)

## Slide 41: Water Surface Profiles http://www.fhwa.dot.gov/engineering/hydraulics/pubs/08090/04.cfm

## Slide 42: Water Surface Profiles-Change in Slope http://www.fhwa.dot.gov/engineering/hydraulics/pubs/08090/04.cfm

## Slide 43: Backwater Profiles
Usually by computer methods
  HEC-RAS
Direct Step Method
  Depth/Velocity known at some section (control section)
  Assume small change in depth
Standard Step Method
  Depth and velocity known at control section
  Assume a small change in channel length