## Slide 1: CTC 261 Hydraulic Devices

## Slide 2: Objectives
Calculate flow through an orifice
Calculate flow over a weir
Calculate flow under a gate
Know how to compute discharge ratings for detention basin outlet structures

## Slide 3: Orifices
Hole in a wall/pipe through which water flows
  Square edge
  Beveled edge

## Slide 4: Orifice
When water flows through an orifice the water contracts with a smaller area than the physical orifice opening (vena contracta)

## Slide 5: General Orifice Equation
Q=ca(2gh).5 This should look familiar!!
Where:
  Q=discharge (cfs or cms)
  c=discharge coefficient (0.62 often used)
  a=cross-sectional orifice area (sq ft or sq meters)
  h=total head (ft or m)
  g=gravitational constant (32.2 or 9.81)

## Slide 6: Orifice Discharge
Free Discharge
Submerged Discharge
Equation is the same. Head for the submerged discharge is the difference between upper and lower water surfaces

## Slide 7: Orifice-Free Discharge
Given: Dia=6”, WSE=220.0 ft;
Elev of orifice centerline=200.0 ft
Q=ca(2gh).5
Q=0.62*0.196*(2*32.2*20).5
Q=4.4 cfs

## Slide 8: Weir
Horizontal surface over which water is allowed to flow
Used to regulate and measure flows
Can have 0,1 or 2 contractions
http://www.flow3d.com/appl/weir.htm

## Slide 9: Contracted Weirs

## Slide 10: Many Weir-types (sharp or broad, cross-section channel shape, weir longitudinal shape)

## Slide 11: Rectangular, Sharp-Crested Weir
Q=cLH3/2
  Q-flow (cfs)
  c-adjusted discharge coefficient (careful)
    c=3.27+0.4(H/P) where P is ht of weir above channel bottom
  L-effective crest length, ft
    L=L’-0.1nH
      L’=actual measured crest length and n=# of contractions
  H-head above crest, ft

## Slide 12: Rectangular, Broad-Crested Weir
Q=cLH3/2
  Q-flow (cfs)
  c-discharge coefficient https://epg.modot.org/index.php/File:749_Broad-Crested_Weir_Coefficients.pdf
  L-crest length, ft
  H-head above crest, ft
Note: Don’t adjust broad-crested weirs for contractions

## Slide 13: V-Notch or Triangular Weir
Q=c*tan(angle/2)*H5/2
  c = 2.5 (but should calibrate)

## Slide 14: Other Weir Types
Cipoletti (trapezoidal)
Ogee (dam spillway)
www.lmnoeng.com
youngiil.co.kr

## Slide 15: Weir/Orifice Equations

## Slide 16: Flow under a gate
Sluice gate, head gate, diversion gate
Depending on conditions, flow can be flat, have a hydraulic jump or be submerged
Flow is modeled as an orifice
Typical c=0.7 to 0.85 but should be determined experimentally

## Slide 17: Siphon flow
Closed conduit that rises above the hydraulic grade line
Has practical problems

## Slide 18: Break

## Slide 19: Detention Outlet Structures
Single Stage (culvert or orifice)
Multi-Staged to handle different flows
Combination of orifices &/or weirs

## Slide 20: Single Stage Outlet Example
An outlet consisting of a 12” pipe is proposed for a detention basin. The invert of the pipe is 320.0 feet and the top of berm is 325.0 ft. Compute the discharge rating for the outlet.
Area=0.785 sq ft
Assume c=0.62
Use orifice equation: Q=ca(2gh).5

## Slide 21: Single Stage Outlet Example
WSE (ft) | h (to c/l of pipe) | Q out (cfs)
320 | 0 | 0
321 | 0.5 | 2.8
322 | 1.5 | 4.8
323 | 2.5 | 6.2
324 | 3.5 | 7.3
325 | 4.5 | 8.3

## Slide 22: Single Stage Discharge Curve
Chart: Stage-Discharge Curve
| 322 | 323 | 324 | 325 | 326 | 327
 | 0 | 2.7632 | 4.786 | 6.1787 | 7.3107 | 8.2895

## Slide 23: Multi-Stage Outlet
4” Orifice @ elevation 560’
Weir w/ L=1.5’ @ elevation 562.67’
Weir w/ L=12.5’@ elevation 563.67’

## Slide 24: Multistage Outlet

## Slide 25: Stage DischargeCurve-Multiple Outlets
Chart: Stage-Discharge Curve
| 560 | 561 | 562 | 562.66999999999996 | 563 | 563.66999999999996 | 564 | 565
 | 0 | 0.39636 | 0.5879 | 0.68698 | 1.5839 | 5.7927 | 15.2657 | 82.3204

## Slide 26: Check Details
Check outflow pipe to make sure it can handle outflow
Orifice would be submerged at some point, impacting h (Note----Q is insignificant compared to the weir flow)