## Slide 1: CTC 450 Review
WW Systems Operations

## Slide 2: Objectives
Understand the basics with respect to advanced WW treatment

## Slide 3: Limitations-Biological Treatment
Doesn’t remove most phosphorous or nitrogen
Incomplete disinfection
Doesn’t remove all toxins
Doesn’t remove non-biodegradable soluble chemicals

## Slide 4: Two systems
Advanced (tertiary and ww reclamation)
  Remove phosphorous
  Convert ammonia to nitrate (nitrification)
  Convert nitrate to nitrogen (denitrification)
  Inactivate pathogens
  Remove heavy metals
  Remove organic chemicals
  Remove inorganic salts
  Eliminate all pathogens

## Slide 5: Excess Phosphorous
“Fertilizes” receiving waters
Causes algal blooms
  Depletes DO
  Reduces water transparency
  Releases foul odors
  Can lose “finer” fish species

## Slide 6: Excess Nitrogen
Ammonia can be toxic to fish/aquatic animals
Can increase eutrophication (but usually phosphorous is limiting)

## Slide 7: Pathogens
Conventional biological treatment
  Up to 99.9% removal
  With disinfection up to 99.99%
  Protozoal cysts and helminth eggs are resistant

## Slide 8: SS Removal-Advanced
Granular-Media filters (similar to water treatment)
Cloth Media filters
Membrane filters

## Slide 9: Pathogen Removal-Advanced
Remove solids first via filtration (pathogens can be protected in the solids)
Chlorination (similar to water treatment)

## Slide 10: Toxic Substance Removal
Toxic-Hazardous to aquatic life or human health
Priority toxic water pollutants-over 100
Evaluating toxicity
  Test influent/effluent for specific substances
  Biomonitor-fathead minnows, water fleas

## Slide 11: Phosphorous Removal
Soluble or organic (organically bound)
Conventional treatment removes 20-40% of phosphorus
Example 13-1 (see next slide)
Advanced treatments
  Chemical-biological
  Reverse osmosis

## Slide 12: Example (Where is the PO43-)
Given the following, trace the inorganic, organic and total phosphorus through a conventional activated-sludge treatment plan.
Assume:
  Primary clarifier removal of 35% BOD
  Primary clarifier removal of 50% solids w/ 0.9% phosphorous
  Activated sludge
    F/M ratio of 0.40 & 2% phosphorus in the sludge
    Filtrate recycles 5% of the influent phosphorus

## Slide 13: Example
Parameter | Raw | After Primary | After Secondary
SS | 240 | 120 | 30
BOD | 200 | 130 | 30
Inorganic N | 22 | 22 | 24
Organic N | 13 | 8 | 2
Total N | 35 | 30 | 26
Inorganic P | 4 | 4 | 3
Organic P | 3 | 2 | 2
Total P | 7 | 6 | 5

## Slide 14: Final Results
70% of P remains in the treated WW
30% of P removed in sludge solids

## Slide 15: Chemical-Biological
Chemicals used
  Alum
  Iron Salts
Chemical-Biological
  Chemicals added in primary clarifiers
  Chemicals added before secondary
  Chemicals added before final clarifier

## Slide 16: Example--Add alum to remove P
If Alum applied to primary tank
18% of P remains in the treated WW
82% of P removed in sludge solids

## Slide 17: Nitrogen-Atmospheric
Atmospheric Nitrogen to Organic Molecules
  Nitrogen-fixing bacteria (rhizobia)
  Live in root nodules of plants (symbiotic relationship)
  Legumes (beans, clover, peas, peanuts,…)
Plants get nitrogen in a usable form
Animals get nitrogen from eating plants
Animals excrete nitrogen as a waste product, usually in the form of ammonia

## Slide 18: Nitrogen
Organic
  Excreted or Decomposed to ammonia
Ammonia
  Nitrosomonas oxidize ammonia to nitrite
Nitrite
  Nitrobacter oxidize nitrite to nitrate
Nitrate
  Under anaerobic conditions via facultative heterotrophs, nitrates are converted to nitrogen gas (which escapes into the atmosphere)
Nitrogen gas

## Slide 19: New Type of Microbe
Ammonia to nitrogen directly
  NH4+ + NO2− → N2 + 2H2O
Anammox (anaerobic ammonium oxidation)
Advantage: No oxygen needed
Strangeness: anammox bugs also produce hydrazine (rocket fuel)
Bugs store the hydrazine in a dense membrane structure of fused carbon rings
Ref: The Invisible Kingdom, Idan Ben-Barak

## Slide 20: Identified in 1999
https://en.wikipedia.org/wiki/Anammox

## Slide 21: Nitrogen in WW
40% ammonia; 60% is bound in organic matter
Usually not enough oxygen is available to convert to nitrites or nitrates

## Slide 22: Nitrogen Removal-Conventional
Primary sedimentation (15% removal)
Biological treatment (another 10%)
Remainder is mainly in the form of ammonia unless oxidation occurs (activated sludge at low BOD loading)

## Slide 23: Nitrogen Removal-Advanced
After biological treatment:
  Aeration
  Final settling
Alkalinity is reduced when nitrification takes place; lime or soda ash is added to maintain alkalinity

## Slide 24: Nitrate removal-Advanced
Nitrate can pollute groundwater
Denitrification converts nitrates to nitrogen gas
Process is anaerobic or anoxic
Process requires an organic carbon source (methanol or raw ww)
Via recycle, denitrification can be placed ahead of nitrification

## Slide 25: EBPR-Enhanced Biological Phosphorous Removal
Anoxic zone (0.5 to 3 hours detention time) followed by aerobic zone (6-24 hrs)
Helps remove both N and P