## Slide 1: Review of Last Lecture
Chemistry Review
Concentrations
Equivalence (expressed as N or P)
Stoichiometry
Gas Solubility
Organic Compounds
Water quality tests

## Slide 2: CTC 450 – Biology Concepts for Water and Wastewater Systems
Kingdom: Eubacterium Scientific Name: Escherichia coli Image Courtesy of: Shirley Owens, Center for Electron Optics, MSU Image Width: 9.5 microns Image Technology: SEM (Scanning Electron Microscope)
http://commtechlab.msu.edu/sites/dlc-me/zoo/zah0700.html

## Slide 4: Objectives
Understand key biological organisms important to water/ww treament
Understand commonly used testing techniques
Know what BOD stands for, how it’s measured and why it’s important

## Slide 5: Waterborne Diseases

## Slide 6: Microorganisms (Biological Treatment

## Slide 7: Organisms
Bacteria
Fungi
Protozoa
Viruses
Algae
Helminths (parasitic worms)

## Slide 8: Microbe Facts (-viruses) Ref: The Invisible Kingdom, Idan Ben-Barak, 2009, ISBN-13: 978-0-465-01887-1
One trillion microbes in a teaspoon of garden soil (10,000 species)
100,000 microbes on a sq cm of human skin
2-4 pounds of microbes on a healthy human body
E.Coli can reproduce 72x per day

## Slide 9: Bacteria
One-celled organisms that reproduce by binary fission
Two major groups:
  Heterotrophs (Pseudomonas sp. shown)
  Autotrophs
  (Nitrobacter sp. shown)

## Slide 10: Heterotrophs
Use organic matter for energy and carbon
  Aerobic
  Facultative
  Anaerobic

## Slide 11: Aerobic
Input: Organics and Oxygen
Output: Carbon dioxide, water and energy

## Slide 12: Anaerobic
Reduce nitrates, sulfates, or organics to obtain energy
Input: Organics, nitrates, sulfates
Outputs: Carbon dioxide, nitrogen, hydrogen sulfide, methane

## Slide 13: Facultative
Can use oxygen (preferred since more energy is obtained) or can use anaerobic pathways
Active in both aerobic and anaerobic treatment processes
Yeast and many bacteria

## Slide 14: Autotrophs
Use inorganic compounds for energy and carbon dioxide as a carbon source
Energy is used to break up carbon dioxide into carbon (used for building cells) and oxygen (byproduct)

## Slide 15: Autotrophs
Earth 4.6 billion years
  Radiometric 3.8/3.9 billion & some of those rocks are sedimentary rocks from erosion of even older rocks
  3.5 billion--fossil evidence—autotrophs
  Created mats called stromatolites
  Photosynthesis – released oxygen (which eventually lead to our current atmosphere)

## Slide 16: Autotrophs
An extremely important group
  Stromatolites
http://www.nvcc.edu/home/cbentley/world_photos.htm
http://gsc.nrcan.gc.ca/paleochron/03_e.php
A geologist reacts enthusiastically to a world-class exposure of stromatolites. I'm imagining doing the backstroke in the Mesoproterozoic Belt Sea where these stromatolites grew. This is in Grinnell Glacier cirque, Glacier National Park, Montana. Up until about ten years ago, this outcrop was mantled by glacial ice, but now Grinnell Glacier has receded almost completely. While I feel sad that the glacier has died, I'm delighted at this view into the Precambrian world. Summer 2007.

## Slide 17: Pangea (300mya); Pangea Ultima

## Slide 18: Autotrophs
Cyanobacteria
  Plug water filters
  Cyanotoxins (potential toxins in drinking water)
Nitrifying bacteria
  Nitrosomonas: Ammonia to Nitrites
  Nitrobacter: Nitrites to nitrates
Sulfur bacteria
  Hydrogen sulfide to sulfuric acid
  Can cause corrosion in pipes
Iron bacteria
  Ferrous iron (2+) to Ferric (3+)
  Causes taste and odor problems

## Slide 19: Waterborne Pathogenic Bacteria
Salmonella sp.
Vibrio Cholerae
Shigella sp.

## Slide 20: Fungi
Microscopic nonphotosynthetic plants including yeasts and molds
Molds are filamentous; in activated sludge systems they can lead to a poor settling floc

## Slide 21: Protozoa/Simple Multi-Celled
Protozoa and other simple multi-celled organisms digest bacteria/algae
Important in secondary treatment of wastewater

## Slide 22: Protozoa
Protozoa Euplotes
rotifer
Amphileptus pleurosigma

## Slide 23: Protozoa/Simple Multi-Celled
Giardia and Cryptosporidium are parasitic protozoa that can cause illness

## Slide 24: Giardia
giardia

## Slide 25: Cryptosporidium

## Slide 26: Viruses
Parasites that replicate only in the cells of living hosts.
Several viruses cause illness and can be waterborne.

## Slide 27: Adenoviruses

## Slide 28: Caliciviruses

## Slide 29: Poliovirus

## Slide 30: Hepatitis A virus

## Slide 31: Algae
Simple photosynthetic plants
Algae are autotrophic, using carbon dioxide or bicarbonates as their carbon source

## Slide 32: Algae Images
http://www.jochemnet.de/fiu/bot4404/BOT4404_5.html

## Slide 33: Lakes/Algae
Oligotrophic-nutrient poor and biologically unproductive
Mesotrophic-Some aquatic plant growth; moderate populations of sport fish
Eutrophic-nutrient rich, tolerant fish that are less desirable

## Slide 34: Whipworm

## Slide 35: Hookworm

## Slide 36: Dwarf Tapeworm

## Slide 37: Factors Affecting Disease Transmission
Latency
Persistence
Infective Dose

## Slide 38: Latency
Period of time between excretion of a pathogen and its becoming infective to a new host
No latency-viruses, bacteria, protozoa, a few helminths
Distinct latency-most helminths (Ascaris lumbricoides-10 days)

## Slide 39: Persistence
Length of time that pathogen remains viable
Least to most: bacteria, viruses, protozoal cysts, helminth eggs (months)

## Slide 40: Infective Dose
Number of organisms that must be ingested to result in disease
  Viruses and protozans-low
  Bacteria-medium
  Helminth-single egg or larva
Definition: Median infective dose is dose required to infect half of those exposed

## Slide 41: Pathogen Categories
I-nonlatent, low infective dose
  viruses, protozoans, dwarf tapeworms
II-nonlatent, medium to high infective dose, moderately persistent
  bacteria
III, Latent, persistent
  Most helminths

## Slide 42: Control by Pathogen Categories
Type I-infections transmitted where personal cleanliness and domestic hygiene are poor. Control: Improve cleanliness and environmental sanitation, including food prep, water supply and wastewater disposal.
Type II-Less likely to be transmitted by person-to-person. Wastewater collection, treatment and reuse are of greater importance, particularly if living standards are high enough to reduce person-to-person transmission
Type III-Less related to personal cleanliness. Important are cleanliness of vegetables grown in fields where reuse of wastewater is used.

## Slide 43: Human Carriers
Proportion of healthy persons excrete pathogens
  Minor or no remaining symptoms but pathogens excreted for months, years or a lifetime

## Slide 44: Sanitation Workers
Wastewater should be considered potentially pathogenic; however…….
Studies show that waterborne diseases are no greater for sanitation workers than population as a whole
Safety precautions include:
  Good personal hygiene
  Prompt medical care if skin is broken
  Precautionary tetanus shots

## Slide 45: Testing for Pathogens
Viruses-special circumstances
Giardia/Cryptosporidium-filter
Coliform-multiple tube fermentation to get MPN (most probable number) or presence-absence

## Slide 46: BOD-Biochemical Oxygen Demand
Commonly used test to define the strength of a wastewater
Quantity of oxygen utilized by microorganisms (mg/l)
Equations are based on initial and final DO measurements (5 days is std.)

## Slide 47: BOD Test
300-ml bottle
20C +/- 1C in air incubator or water bath
Dilution water is saturated w/ DO and contains phosphate buffer, magnesium sulfate, calcium chloride and ferric chloride
Test includes several dilutions as well as blanks

## Slide 48: BOD equation (non-seeded)
BOD5=(D1-D2)/P
BOD5=BOD in mg/l
D1=initial DO of the diluted wastewater sample approx. 15 minutes after preparation, mg/l
D2=final DO of the diluted wastewater sample after a 5-day incubation, mg/l
P=decimal fraction of the wastewater sample used (ml of ww sample/ml volume of the BOD bottle)

## Slide 49: BOD Rate constant
Important in designing secondary WW systems
Can be estimated graphically from BOD data
Typical value is 0.1-0.2 per day
Can calculate theoretical BOD at other time values from equation if constant is known or estimated

## Slide 50: Unseeded BOD example
Data from unseeded domestic wastewater BOD test:
  5 ml of WW in a 300-ml bottle
  Initial DO of 7.8 mg/l
  5-day DO of 4.3 mg/l
Compute BOD5 and calculate BODult assuming a k rate of 0.1 per day

## Slide 51: Unseeded BOD Example
BOD5=(D1-D2)/P
D1=7.8 mg/l
D2=4.3 mg/l
P= 5 ml / 300 ml
BOD5=(D1-D2)/P=210 mg/l

## Slide 52: Unseeded BOD example Calculate Ultimate BOD
BODt= BODult(1-10-kt)
BOD5= BODult(1-10-kt)
210= BODult(1-10-(0.1)(5))
BODult= 310 mg/l

## Slide 53: BOD-seeded
Industrial ww may not have the biological organisms present to break down the waste
ww must be seeded with microorganisms to run the BOD test (a BOD test is also run on the seed itself)
BOD equation is modified to account for the oxygen demand of the seed

## Slide 54: BOD equation (seeded)
BOD5=[(D1-D2)-(B1-B2)f]/P
BOD5=BOD in mg/l
B1=DO of the diluted seed sample approx. 15 minutes after preparation, mg/l
B2=DO of the seed sample after a 5-day incubation, mg/l
f=ratio of seed volume in seeded ww to seed volume in BOD test on seed(ml of seed in D1/ml of seed in B1)

## Slide 55: Seeded BOD example
Data from a seeded meat-processing wastewater BOD test:
  Estimated BOD of ww is 800 mg/l
    D1=8.5 mg/l and D2=3.5 mg/l
  Seed has a BOD of 150 mg/l
    B1=8.5 mg/l and B2=4.5 mg/l
What sample portions should be used for setting up the middle dilutions of the ww and seed tests ? What is the ww BOD?

## Slide 56: BOD Dilution Table

## Slide 57: Seeded BOD example
Using Table 3-4:
  For WW—add 1-2 ml (estimated BOD=800)
  For seed—add 5-10 ml (estimated BOD=150)
Using BOD5=(D1-D2)/P (& assuming delta D of 5 and solving for numerator in P):
  Add 1.875 ml (round off to 2 ml) for ww
  Add 10 ml of seed to BOD test of seed
10% of seed=1 ml added to ww BOD bottle as seed

## Slide 58: Seeded BOD example
BOD5=[(D1-D2)-((B1-B2)f)]/P
BOD5=[(8.5-3.5)-(8.5-4.5)(1/10)]/(2/300)
BOD5 =690 mg/l

## Slide 59: Temp Affects Growth Rate

## Slide 60: Temperature-Most WW systems operate in the mesophilic range

## Slide 61: Yellowstone

## Slide 62: Yellowstone

## Slide 63: Yellowstone

## Slide 64: Old Faithful