## Slide 1: CTC 450 Review
Class Requirements
Water treatment exercise
  Private
  Public
Wastewater treatment exercise
  Private
  Public

## Slide 2: Objectives
Students have the ability to:
Define the chemical properties of water
Use stoichiometry to calculate concentrations
Determine “equivalent” concentrations
Understand the major laboratory water analysis tests

## Slide 3: Water Distribution on Earth
Oceans 97.13%
Polar Ice Caps and Glaciers 2.24%
Groundwater 0.61%
Rivers, lakes, streams 0.02%

## Slide 4: Water Chemistry
Water contains various inorganic and organic compounds from contact with solids or gases
Water is dipolar (+ & - charged areas) which affects the solubility of solids (dissolved ions)
www.shorstmeyer.com/ wxfaqs/float/watermolec.html
www.brooklyn.cuny.edu/.../ SD.PS.LG.Water.html

## Slide 5: Water-Molecular Weight
Usually 18 (16+1+1)
3 isotopes of hydrogen
  H-1 Protium (one proton)
  H-2 Deuterium (one proton; one neutron)
  H-3 Tritium (one proton; two neutrons)
3 stable isotopes of oxygen
  O-16 (8 protons; 8 neutrons)
  O-13 (8 protons; 5 neutrons)
  O-15 (8 protons; 7 neutrons)

## Slide 6: Common Elements
Common elements we’ll use can be found in Table 4-1 of your book (pg 78)
The table contain the element name, symbol, and the atomic weight
Oxygen (O); 16
Hydrogen (H); 1
Atomic weight of water is 18 (16+1+1)

## Slide 7: Table 4-1 elements

## Slide 8: Common Inorganic Compounds
Common compounds we’ll use can be found in Table 4-2 of your book (pg 79)

## Slide 9: Table 4-2 compounds

## Slide 10: Definitions
One mole of a substance contains 6.024 x 1023 molecules or atoms
The molar mass is found by adding the atomic weights of the elements in the compound
  1 mole of NH3 has 6.024 x 1023 molecules and weighs 17 grams (14 grams for nitrogen plus 3 grams for 3 hydrogen elements)
The equivalent weight is the molecular weight divided by the valence or electrical charge

## Slide 11: Expressing Concentrations
Mass Concentration
Molar Concentration
Equivalents and Normal Concentration

## Slide 12: Mass Concentration
Mass of solute per volume of solution
Milligrams per liter (mg/l)
  Equivalent to parts per million (ppm) for most natural waters and wastewaters since 1 liter of water has a mass of 1 kg (1E6 mg)
  Remember: mg/l = ppm

## Slide 13: Molarity/Molality
Molarity-Moles of solute per volume of solution
  A 1 molar solution of NaCl would contain 58.5 gm per liter of water
Molality-Moles per mass of water
Equilibrium constants are based on molar concentrations

## Slide 14: Equivalents and Normal Concentration
The equivalent weight of an element or radical is equal to its atomic weight divided by the valence it assumes in compounds. The definition is based on reaction type.
Advantage is that the number of equivalents of reacting constituents is equal to the number of equivalents of product.
Disadvantage is that a single substance can have two different equivalent weights because the substance is involved in different reactions
A one normal solution contain one equivalent weight of a substance per liter of solution

## Slide 15: Equivalents and Normal Concentration - Example
Oxygen has an atomic weight of 16.0 and always assumes valence 2 in compounds, so its equivalent weight is 8.0
Iron (atomic weight 55.8) has an equivalent weight of 27.9 in ferrous compounds (valence 2) and 18.6 in ferric compounds (valence 3)
In general the normality is the molarity times n where n is either the ion charge or number of protons, hydroxyl ions or electrons transferred in a reaction
  The normality of a solution is never less than the molarity.

## Slide 16: Expressing Concentrations in Terms of another Compound
Elements can exist in different forms
  Nitrogen
    Ammonium (NH4+)
    Nitrite (NO2-)
    Nitrate (NO3-)
  Phosphorous
    Ortho (PO43-)
    Monohydrogen (HPO42-)
    Dihydrogen (H2PO4-)

## Slide 17: ATP/ADP
http://hyperphysics.phy-astr.gsu.edu/hbase/biology/atp.html

## Slide 18: Expressing Concentrations in Terms of another Compound
Hardness and alkalinity are often expressed in terms of CaCO3 (Calcium Carbonate)
The various forms of nitrogen (ammonium, nitrite, nitrate) are expressed as elemental nitrogen (N)
The various form of phosphorous are expressed as elemental phosphorous (P)

## Slide 19: Steps for expressing compounds in terms of another compound/element:
Find the molecular and equivalent weights of all compounds/elements
Use ratios (equivalent wt ratios)

## Slide 20: Example: Expressing Nitrogen Compounds in Terms of N
Example 1/3 (Problem statement):
Express the following in terms of Nitrogen:
360 mg/l (NH4+)
1240 mg/l (NO3-)

## Slide 21: Example (2/3)
Find the molecular weight of all compounds/elements
  N 14 grams (elemental Nitrogen)
  NH4+ 18 grams
  NO3- 62 grams
  Equivalent weights are same as MW

## Slide 22: Example (3/3)
Use ratios to convert compounds to N
  360 mg/l of ammonia *
  (14 mg N / 18 mg ammonia)
  = 280 mg/l ammonia as nitrogen
  1240 mg/l of nitrate *
  (14 mg of N / 62 mg nitrate)
  = 280 mg/l nitrate as nitrogen

## Slide 23: PH Scale
A small amount of water dissociates into H+ and OH- w/ a concentration of hydrogen ion equal to 10-7 moles per liter
pH=inverse of the hydrogen ion conc.
pH at neutrality=7
pH<7 indicates acidity (acid range)
pH>7 indicates alkalinity (basic range)

## Slide 24: Chemical Reactions
Chemical reactions can be manipulated to change water quality
  Add chemicals to precipitate out solids (remove turbidity)
  Raise pH to convert ammonia ions to ammonia gas (remove nitrogen)
  Add lime to precipitate out calcium carbonate (remove hardness)

## Slide 25: Concentrations and Flows to Mass Rate (Tips)
Units
50 mg/l is equal to 50 mg per 1E6 mg
8.34 pounds per gallon (water)

## Slide 26: Chemical Reactions
Class Exercise

## Slide 27: Chemical Equilibrium
Some reactions are irreversible (example-turns into a solid and precipitates out)
Many chemical reactions are reversible to some degree; they’ll eventually reach “equilibrium”---reactant and product concentrations stay the same

## Slide 28: Chemical Reactions
Reactions occur at different rates
  Some reaction rates don’t depend on concentrations (zero order)
  Some reactions rates depend on concentrations (first/second order)
  Temperature can affect rates
http://en.wikipedia.org/wiki/Chemical_kinetics

## Slide 29: Reaction Rates
http://chemistry-helper.blogspot.co.uk/2011/04/distinguish-between-terms-rate-constant.html

## Slide 30: Rate Constant k
https://www.chem.fsu.edu/chemlab/chm1046course/integrated.html

## Slide 31: Stoichiometry
The quantitative relationship between chemical substances in a reaction

## Slide 32: Example: Stoichiometry (1/4)
Adding Lime to Remove Hardness:
CaO+Ca(HCO3)2=2CaCO3 +H2O
What dosage of lime (purity of 78%) is required to combine w/ 70 mg/l of calcium?
Note: The hardness is expressed as calcium

## Slide 33: Example (2/4)
In this case the reaction is balanced. If not balanced, then balance.

## Slide 34: Example-Find Molecular and Equivalent Weights (3/4)
Ca(HCO3)2 162 81
Ca 40.1 20
CaO 56.1 28
56 grams of CaO combines w/ 162 grams of Ca(HCO3)2
Also, 70 mg/l Ca is equivalent to 283 mg/l of Ca(HCO3)2 ====70*(81/20)

## Slide 35: Example (4/4) Use ratios & correct for purity
(28/81)*(283)=98 mg/l CaO
But lime has a purity of only 78%
So 98/.78=126 mg/l CaO ANSWER
56 grams of CaO combines w/ 162 grams of Ca(HCO3)2
Also, 70 mg/l Ca is equivalent to 283 mg/l of Ca(HCO3)2

## Slide 36: Gas Solubility
Oxygen is soluble in water. The oxygen concentration is dependent on temperature, elevation, and chloride concentration
Carbon dioxide is soluble in water
Chlorine is soluble in water

## Slide 37: Colloids
Small particles that don’t settle out
Removed by coagulants (salts of aluminum or iron)
Hydrophilic (hard to remove)
Hydrophobic (easier to remove)

## Slide 38: Solids
Suspended Solids (retained on a filter)
Dissolved Solids (pass through a filter)-if evaporated and measured—TDS (total dissolved solids)
Volatile Solids (those solids that burn off at 550C in a furnace)

## Slide 39: Organic Compounds
Organic compounds contain carbon atoms attached to each other in chains
Common elements that are attached are hydrogen and oxygen
Common organic compounds are hydrocarbons, alcohols, aldehydes, ketones, and carboxylic acids

## Slide 40: Common Lab Tests
Standard Methods for the Examination of Water and Wastewater, Published jointly by the American Public Health Association, American Water Works Association, and Water Environment Federation
  23nd edition 2017
  Available at AWWA

## Slide 41: Common Lab Tests
pH, turbidity, DO—meters & probes
Alkalinity, Acidity, Ammonia, Hardness, COD – titration
Iron and Manganese - spectrophotometer
Trace metals – atomic absorption spectrophotometer
Color, Fluoride, Chlorine, Nitrite, Nitrate – colorimeter
Solids (suspended, dissolved)-filters, drying, weighing

## Slide 42: Probes

## Slide 43: Colorimeter Spectrophotometer
http://www.newton.dep.anl.gov/askasci/chem03/chem03728.htm

## Slide 44: Atomic Absorption Spectrophotometer

## Slide 45: Review Questions
In this class what concentration is typically used:
  Mass
  Normal
  Molar
A mg/l is equivalent to ??=
What does DO stand for?
Neutral pH is?