## Slide 1: CTC 450
Energy Equation

## Slide 2: Review
Bernoulli’s Equation
  Kinetic Energy-velocity head
  Pressure energy-pressure head
  Potential Energy
EGL/HGL graphs
  Energy grade line
  Hydraulic grade line

## Slide 3: Objectives
Know how to apply the energy equation
Know how to incorporate head losses, turbines, and pumps into EGL/HGL graphs

## Slide 4: Energy Equation
Incorporates energy supplied by a pump, energy lost to a turbine, and energy lost due to pipe friction and other head losses (bends, valves, contractions, entrances, exits, etc)

## Slide 5: Energy Equation-In words
PE+Pressure+KE+Pump Energy=
PE+Pressure+KE+Turbine Losses+Head Losses (pipe and other)

## Slide 6: Energy/Work/Power
Work = force*distance (in same direction)
Power = work/time
Power=pressure head*specific weight*Q
Watt=Joule/second=1 N-m/sec
1 HP=550 ft-lb/sec
1 HP=746 Watts

## Slide 7: Energy Examples
For homework review the following 3 example problems located in Brightspace:
Pump Example
Transition Example (contraction)
Reservoir Example (pumped storage)

## Slide 8: Energy Equation-Pump Example
A pipe is 50-cm in diameter and carries water at a rate of 0.5 cms. Before a pump, the elevation of the pipe is 30 meters in elevation and the pressure is 70 kPa. After the pump, the pipe is 40 meters and 350 kPa. Assume the head loss is 3 meters.
What power in kilowatts and horsepower must be supplied to the flow by the pump?

## Slide 9: Energy Equation-Pump Example (Continued)
Calculate velocities before and after pump:
Before & after pump velocity=2.55 m/sec
If velocities are the same then what????

## Slide 10: Energy Equation for Pump Example
PE+Pressure+Pump Energy=
PE+Pressure+Losses (other)

## Slide 11: Energy Equation-Pump Example1
Before pump:
Pressure=70 kPa
Potential energy=30m
Power supplied by pump=?
After pump:
Pressure=350 kPA
Potential energy=40 m
Head loss=3m (unclear-assume pump head loss?)

## Slide 12: Energy Equation-Pump Example2
Solve for energy supplied by pump:
41.5 meters
28.5 m (increase pressure from 70-350 kPa)
10 m (increase in elev of 10m after pump)
3 m (overcome friction loss)
What power in kilowatts and horsepower must be supplied to the flow by the pump?

## Slide 13: Energy Equation-Pump Power
What power in kilowatts and horsepower must be supplied to the flow by the pump?
Power=head*specific weight*Q
Power=206 kilowatts
Power=276 horsepower

## Slide 14: Hints for drawing EGL/HGL graphs
EGL=HGL+Velocity Head
Friction in pipe: EGL/HGL lines slope downwards in direction of flow
A pump supplies energy; abrupt rise in EGL/HGL
A turbine decreases energy; abrupt drop in EGL/HGL
When pressure/velocity=0, the HGL=EGL=water surface elevation
Steady, uniform flow: EGL/HGL are parallel to each other
Velocity changes when the pipe diameter changes
If HGL<pipe elev., then pressure head is negative (vacuum-cavitation)

## Slide 15: Transition Example
Flow in a pipe goes through a transition (contraction).
Q=0.707 cms
D1=30 cm
D2=20 cm
Head loss due to contraction = 2.6 m
P1=250 kPa
P2=? (Answer=22 kPA)

## Slide 16: Reservoir Example
A pump draws water from a reservoir, where the WSE=520 ft, and forces the water through a pipe 5,000 feet long and 1 foot in diameter.
The pipe then discharges the water into a reservoir with WSE=620 ft.
The flow rate is 7.85 cfs and the head loss is 77.6 feet.
Determine the head supplied by the pump and the power supplied to the flow.

## Slide 17: Reservoir Example Answers
Head supplied by the pump is 177.6 ft (100’ to raise water to an increased elevation and 77.6’ to overcome friction loss in the pipe)
Power supplied by the pump=158 hp

## Slide 18: EGL/HGL (pipe elev. Increasing)

## Slide 19: Another EGL/HGL example

## Slide 20: EGL/HGL (Pump)

## Slide 21: Next Lecture
Head loss due to friction
Other head losses