## Slide 1: CTC 450 Sustainability-Water &Wastewater

## Slide 2: Objectives
Understand the ideas of sustainability and carbon footprint, and be able to apply them to water and wastewater processes

## Slide 3: Sustainability
Maintain, Support, Endure
Steady-State
Brundtland Commission of the United Nations on March 20, 1987: “sustainable development is development that meets the needs of the present without compromising the ability of future generations to meet their own needs.”
Living on the sun’s energy in real-time.

## Slide 7
https://flowcharts.llnl.gov/

## Slide 9: Summary (Petroleum)
2002: 39.2 Quads (38% domestic/62% imported)
2012: 34.7 Quads
2013: 35.1 Quads
2015: 35.4 Quads (**52% domestic/49% imported)
2021: 35.1 Quads
**In 2015: 18-19 MBPD Consumed;
9.3 MBPD Produced; 8.7 MBPD Imported

## Slide 14: Greenhouse Gasses
Usually CO2 (but also CH4 and others)

## Slide 15: Current CO2 Concentrations (Mauna Loa)

## Slide 16: Information on Greenhouse Gas Links
Greenhouse Gas Protocol-Corporate Standards
https://ghgprotocol.org/corporate-standard
Emissions Inventory
http://www.epa.gov/climatechange/ghgemissions/usinventoryreport.html#overview

## Slide 17: From Emissions Inventory

## Slide 18: Measuring Carbon Footprint
Greenhouse Gas Protocol: A Corporate Accounting and Reporting Standard
Scope 1 (Direct Emissions)
Scope 2 (Purchases of Electricity)
Scope 3 (Misc-Employee Commuting, Materials, Waste Disposal)

## Slide 19: Carbon Footprint: Water Systems
Scope 1-None
Scope 2-Significant (Electricity)
Scope 3-Minimal (Chemicals)

## Slide 20: Carbon Footprint Electricity Consumption: Water Systems
Electricity Consumption:
  200 kWh/MG (Low)
  2,000 kWh/MG (Conventional)
  35,000 KWh/MG (High)
Low (gravity, chemical disinfections, delivery-close and flat)
Conventional (river or shallow well, clarification-filtration, delivery-distributed-flat)
High (deep well or long delivery, desalination, distribution-hilly)

## Slide 21: CO2 Emissions Coefficients for Electric Power (Metric Tonnes/MWh)
Old Book Appendix, page 444
0.013-Idaho, Vermont
0.111-Washington
0.275-California
0.389-New York
1.017-North Dakota
Original Source: EIA (March 2002)

## Slide 22: Carbon Footprint: WW Systems
Scope 1-Significant (CH4, NOx)
Scope 2-Significant (Electricity)
Scope 3-Minimal (Chemicals)

## Slide 23: Carbon Footprint Electricity Consumption: WW Systems
Electricity Consumption:
  1,600 kWh/MG (Low)
  3,000 kWh/MG (Conventional)
  9,200 KWh/MG (High)
Low (gravity, fixed film, composting/land application, gravity discharge)
Conventional (lift at plant, activated sludge, digestion and land application, pump for discharge)
High (multiple pumping to plant, advanced treatment, pelletization, significant discharge pumping)

## Slide 24: Becoming Carbon Neutral-WW
Use anaerobic digestor gas for heat and power generation (cogen)
Energy Conservation
Add renewable energy
Optimize chemicals
Manage waste (reuse; fertilizer)
Green facilities (LEED)
Manage Watershed

## Slide 25: Advanced WW Treatment
Requires more energy but will allow more reuse
Analysis is needed

## Slide 26: LEED-Leadership in Energy and Environmental Design
https://www.usgbc.org/leed