## Slide 1: CTC 450 Review
Advanced WW Treatment
  Removal of nitrogen
  Removal of phosphorus
  Complete removal of pathogens
  Removal of other toxics

## Slide 2: Objectives
Understand the basics with respect to reusing wastewater

## Slide 3: Reuse
Reuse is defined as direct application of treated WW for agricultural and urban irrigation, industrial reuse, groundwater recharge, and others
Discharging WW to a receiving water that is ultimately used downstream for a water source is not considered reuse (dilution/separation in time and space)

## Slide 4: Water Reuse - Functions
Treated effluent is used as a water resource for beneficial purposes
Effluent is kept out of streams, lakes and beaches

## Slide 5: Water Reuse – Main Concerns
Reliable treatment of WW
Protection of public health
Public acceptance

## Slide 6: Matter of Economics
Water reuse may be less costly:
  Use N/P for irrigation instead of providing tertiary processes to prevent eutrophication
  Water shortages – a future possibility (CA/AZ/FL)

## Slide 7: Potential Drawbacks
Pathogens via physical contact or aerosols
Public perception

## Slide 8: Water Statistics
Recycled WW
  983 MGD (1995)
  2% of total wastewater release (41,000 mgd)
  CA/AZ/FL account for majority

## Slide 9: Water Quality Effluent Stds
Dependent upon reuse application
  Agricultural irrigation (restricted-with respect to human activity)
    fodder,fiber,seed crops
  Agricultural irrigation (unrestricted)
    processed food, food eaten raw
  Urban irrigation (restricted)
    Golf courses, cemeteries, highway medians
  Urban irrigation (unrestricted)
    Parks, playgrounds, residences, comml landscaping

## Slide 10: Advantages/Disadvantages of Agricultural Irrigation
Already contains nutrients and soil amendments
Agricultural areas may be nearby
Money for cash crops
In arid regions, ww may be the only source of water
Nitrate - groundwater
Heavy metals - soils
Pathogens - farm workers

## Slide 11: Agricultural Irrigation
Storage required to balance supply/demand

## Slide 12: Design of Irrigation Systems
Balance water to determine storage requirements
Balance nitrogen to prevent migration (do not want a buildup of nitrogen)

## Slide 13: Urban Irrigation
Cross-connections prohibited
Color-code pipes
Warning signs
Reuse water pipes 3’ below potable water

## Slide 14: Underground Utilities

## Slide 15: Groundwater Recharge
Surface infiltration (surface spreading)
Direct injection
Issues
  Fate of particulates
  Fate of bacteria/viruses
  Fate of dissolved organic/inorganic constituents (particularly toxics)

## Slide 16: Groundwater Recharge-Standards
US federal requirements/standards have not been established
Currently regulated by state agencies

## Slide 17: Storage Issues
Need for storage
Type (open or closed)
Discharge requirements
Problems:
  Odors, loss of chlorine residual, low DO
  Temperature stratification, bird/rodents
  Algal blooms, regrowth of microorganisma

## Slide 18: Agricultural Irrigation-Example Tallahassee, FL
2000 acres;
16 pivot irrigators
  irrigators controlled by computer
  low-drift nozzles
Vegetation-canola, corn, sorghum, grass
Monitoring wells
Capacity-23 mgd
Four parallel treatment plants

## Slide 19: Residential Lawn Watering El Dorado Hills, CA
Dual plumbed distribution system
66 mg reservoir
Drip irrigators-no restriction times
Spray irrigators-restricted to 9pm-6am
Back-up: potable lake water
  Plant doesn’t meet required water quality
  System can’t meet peak irrigation demands

## Slide 20: Urban Reuse St. Petersburg, FL
Irrigation of parks, school, golf courses, comm’l and residential irrigation
Some water injected into deep-well system
Effluent requirements:
  SS-5 mg/l (in practice 1-3 mgl/l)
  Chlorine residual-1 mg/l after 15 min (in practice 4 mg/l)

## Slide 21: Industrial Reuse Los Medanos Energy Center, CA
WW treatment plant provided recycled water to the energy center
Water is used for the heat recovery steam generator make-up and water for the evaporative cooling system
Treatment processes:
  Dual-media, ultra- and activated carbon filtration for TOC removal
  Antiscalant chemical added for evaporative system
  Reverse osmosis for evaporative cooling

## Slide 22: Final Exam Problems
Water Processing-Clarifier following Coagulation (25 pts)
Wastewater Processing-Trickling Filter (25 pts)
Wastewater Processing-Clarifier (25 pts)
Solids Mass Balance (25 pts)

## Slide 23: Final Exam Review
Open book/open notes/
Can use computer/cell phone for electronic book
No old tests
Show all work
Know the standards
Don’t forget units
Conversions-concentration to mass