## Slide 1: CTC 450 Review
Water Processes

## Slide 2: Objectives
Understand the basics with respect to operation of waterworks

## Slide 3: Operational Requirements
To maintain a system in working order (and avoid as much as possible any failures) ……..
you must know as much as possible about the overall system

## Slide 4: Fire Hydrants
Restrict usage for street cleaning & construction
After use, check operation
Periodic inspections
Maintain a stock of repair parts
Drainage essential in cold climates

## Slide 5: Fire Hydrants (4 ways they break)
Blunt force trauma (cars)
Cold weather
Valves cranked too hard
Unofficial use (children/contractors)

## Slide 6: Valves
Installed to isolate sections of pipe
Provide periodic inspection and maintenance
Must know where they’re at to use them (good mapping; don’t pave over)
Repair or replace if needed

## Slide 7: Service Connections
Service pipe from the main (corporation stop)
Usual minimum service pipe diameter is ¾”
Curb box/stop (valve to turn off water to building)

## Slide 8: Tapping Mains
Wet tap—pipe is tapped while in use

## Slide 9: Example of Responsibility

## Slide 10: Cross Connection, Backflow Preventers and Meters
Inspect areas of potential high hazard (hospitals, mortuaries, industries, irrigation systems, etc)
Meters must be repaired or replaced if not working correctly

## Slide 11: Pipeline Installation
Mains installed at a depth to prevent freezing
Compacting backfill and trench design/installation increases pipe support
Water/sewer lines should be separated at least 10’ horizontally and water should be 18” higher than sewer

## Slide 12: Pressure Testing
There is always some leakage
Leakage tests are performed and compared to a standard

## Slide 13: Thrust Restraints (pressure/velocity)
Use some type of restraint (concrete thrust block/joint restraint) to anchor pipelines at:
-dead ends
-bends
-changes in horizontal/vertical directions

## Slide 14: Leak Detection
Find small leaks before they become large
Can use sound wave detectors to detect leaks
Can fix small leaks by fitting a cover over the pipe

## Slide 15: Distribution Testing
Fire Flow Tests
Hydrant Tests (pressure and flow)
  Minimum 20 psi @ designated fire flow
  Dechlorinate water (vitamin C) if discharged to storm system
Flow and pressure testing to calibrate computer models

## Slide 16: Water Treatment Process Control
Highly automated with dial-in capabilities
SCADA systems (supervisory control and data acquisition)

## Slide 17: Water Quality Control
Some lab tests are on-line (turbidity)
Some tests are done on-site
Some tests are sent out

## Slide 18: Sanitary Survey
Review of system to identify all areas that represent a risk to water quality and delivery

## Slide 19: Recordkeeping
Efficient management depends on detailed recordkeeping
  Water quality
  Water quantity
  Plant operation data
  Chemicals added
  Annual reports
  Public notification

## Slide 20: Water Conservation
Public education
Installation of high-efficiency plumbing fixtures
  Tampa-77.2 gpcd to 38.9 gpcd
Institute water rates/meters (discourage lawn watering)
Fix leaks

## Slide 21: Energy Conservation
Pumps major use of energy
Must understand rate schedule of utility
Can replace motors with high-efficiency motors

## Slide 22: Water Rates
Must charge enough to cover costs
Usually charged by class (residential, commercial, or industrial)

## Slide 23: Security
SCADA systems should be secure
Fire protection
Prevention from contamination and ability to determine contamination
Barriers around perimeter
Use of card keys, cameras, and strict protocols

## Slide 24: Rehabilitation
240,000 water main breaks per year
Have a plan for water main breaks (parts/tools/equipment)

## Slide 25: Cleaning
Periodically remove sediment (dead-end branches)
Buildup on pipes can occur-reduces hydraulics capacity (maintain proper pH; use scraper/cutting tools).

## Slide 26: MVWA (MVW.US)
All kinds of information can be found on website of local water authorities